## Slide 1
2.5 G GSM/GPRS LOCOSTO-IC DBB
TI proprietary Information, under Non-Disclosure Agreement
Texas Instruments Shanghai
Wireless Customer Integration & Design Center

## Slide 2: AGENDA
SYSTEM OVERVIEW
DBB OVERVIEW
ARMIF
EMIF
SYSTEM DMA
CLOCK MANAGEMENT
CAMERA APPLICATION
EXTERNAL PERIPHERALS
SECURE ENVIRONMENT

## Slide 3: LOCOSTO-IC SYSTEM OVERVIEW
LOCOSTO-IC
SYSTEM OVERVIEW
TI proprietary Information, under Non-Disclosure Agreement

## Slide 4
Locosto+:
  Serves the GPRS hi-end market
  Support the high end requirements such as Camera, MP3 player, Midi32, Stereo, BT, IrDA
  Supports a fairly rich Application suite
Locosto:
  Serves the entry GSM/GPRS market with basic feature sets
  Midi16, camera
  Supports basic Application suite
LocostoLite
  Serves GSM only market
  Supports Basic Messaging functions
LOCOSTO-IC CHIPSET OVERVIEW

## Slide 5
LOCOSTO-IC CHIPSET OVERVIEW
  TCS2300: TI low-cost ChipSet, addressing 2.5G
  LoCosto-IC: GSM/GPRS SoC (C027 /90nm ASIC lib)
    Digital Base Band structure (ARM7/c54x)
    Radio Frequency Sub-System (DRP2.0)
  Triton Lite: Analog Base Band chip (A07 TI Analog process)
    Voice & Stereo Audio
    Power & Battery management
    RTC, USB Transceiver…
  TCR3.2x: Software layer (TCR3.1x Based)
    Modem GSM/GPRS
    Applications suite

## Slide 6: LOCOSTO-IC CHIPSET OVERVIEW
External/Extra Sub-System Supported
    LoCosto-IC
      Flash
      SIM Card
      KeyBoard
      Color LCD
      USB 1.1, Full-Speed, Client
      26MHz Crystal
      Power-Amplifier
      Front-End Module
      TI-Bluetooth (BRF6150) Wireless Short-Distance Connectivity
      TI-AGPS /TWL5002 localization system (I/F provision)
      Digital Camera systems.
      UART Cable or IRDA
      FM Radio receiver (ex. Philips TEA5767/68…)
      NandFlash
      CarKit &/ USB charger

## Slide 7: LOCOSTO-IC CHIPSET OVERVIEW
Basic External Sub-System:
    TriTon Lite
      HandSet Microphone & Speaker
      HeadSet Mono/Stereo-Audio speakers & microphone connection
      Melodie-Ringer (HandFree) &/ Buzzer
      Battery Pack (Nimh/Li-ion) & 6-7V Reg or 20V Non-Reg Charger
      Vibrator motor control
      RTC 32KHz crystal

## Slide 8: LOCOSTO-IC CHIPSET OVERVIEW

## Slide 9
DMA
CDSP subchip
Power
Management
Voice
Codec
Audio
Codec
USB-OTG
transceiver
I2S
I2C
LCD
RAM
NOR
FLASH
NAND
FLASH
LOCOSTO-IC CHIPSET OVERVIEW
BT
AGPS
32 kHz
On/Off
LED
TRITON LITE
ADC aux
Bus Cntl
RTC
LOCOSTO
EMIF
ARM7TDMIE
13 Mhz
ULPD
On_nOff
Wakeup_int
MB
BB
I2C
I2C
LCD
KB
Camera
Companion Chips
NandFlashIf
Cport
Keyboard
VSP
26 MHz
DRP
I2C
Mcsi
UART
32 Khz
SPI
Secondary
LCD
USIM
PA
+
Antenna

## Slide 10
LOCOSTO-IC Hardware Architecture
Notes: 7.4.4.10 Pulse Width Tones (PWT)
These modules generate a modulated frequency signal for an external buzzer.
The PWT frequency is programmable between 349Hz and 5276Hz with 12 half tone frequencies per
octave. The volume is also programmable.
7.4.4.11 Pulse Width Light (PWL)
These modules allow controlling the backlight of a LCD and/or a keypad
The PWL voltage level control technique, based from a 4096bit random sequence, decreases the
spectral power at the modulator harmonic frequencies. The logic operates from the 32KHz reference
clock to be independent from the system activity mode.
7.4.4.12 Light Pulse Generator (LPG)
This module produces the electrical signal for a blinking LED.
The blink period and duration are programmable.
The logic operates from the 32KHz reference clock to be independent from the system activity mode.

## Slide 11: DBB Generic SoC Functions
DPLL & CLKM
  System Clock & Reset Control.
DMA
  Direct Memory Access
EMIF
  External Memory Interface
Interrupt Handler & Secure Interrupt handler
  Main INTH 31 lines
  Secure INTH 5 lines
IO Configuration
  I/O’s mode selection (Multi-function I/O’s, Test & debug…)
Notes: System-On-Chip (SOC)

## Slide 12: DBB Generic SoC Functions (continue)
2 General-Purpose Timers.
  Auto-Reload / One-Shot modes.
  Interrupts upon underflow.
  13MHz clocking source.
1 Watch-Dog or General-Purpose Timer.
  Same as above or watch-dog timer (default)
  13MHz/14 clocking source.
Debug Unit
  64 x 32-bit words FIFO
  Continuous data record (MCU clock-cycle based)
JTAG & eFuse Controller
  Manufacturing, Test & Debug Facilities…

## Slide 13: Dedicated Peripherals (Rhea Bus)
  Ultra Low-Power Down controller (ULPD)
      Power-ON/Down & Deep-Sleep mode management
      Maintains GSM time base from the 32KHz low-power reference clock
  Time Processing Unit (TPU)
      2 ports RAM of 1024 words of 16 bits scenario’s storage unit
      micro-instructions based Scheduler
      Real Time control (GSM Q-Bit) of RF & Analog (TSPACT 7-int / 9-Ext)
  RF Transceiver; Digital Radio Processor (DRP2.0)
  GPRS Encryption Algorithm (GEA1/2/3)
      Support Frame Check Sequence & ciphering/deciphering mode 1,2 and 3. (GSM 01.61, 04.64 recommendations).
  GSM Cipher-processor (A51/2/3)
      implements A51, A52 (GSM Rec03.20) and new A5/3 Kasumi algorithm (GSM/EDGE Cipher algorithm)

## Slide 14: Dedicated Peripherals (Rhea Bus)
  USIM Interface
      GSM SIM-card controller
      H/W management for T-0 and T-1 transmission protocols, (ISO7816.3 )
  2 I2C H/W-controller @400Kbps (1 MCU + 1 DSP /same bus I/F)
      TriTon Lite ABB (Power, USB-Xcvr, Voice & Stereo Codec’s, RTC)
  1 C-port/I2S Audio-Stereo Codec serial interface
      Slave up to 3.072Mbps (Exclusive Static sharing DSP/MCU)
      TriTon Lite ABB (Stereo-Audio codec data )
  1 Voice Serial Port Slave @500kbps (cDSP internal TI-Bus)

## Slide 15
  All connectivity interfaces support a 1.8V maximum voltage
  with the exception of the USIM pin’s that are 3V compliant.
  RHEA Bus (MCU &/ cDSP) @52Mhz
      1 Enhanced Keyboard controller
        Up to 5-Row x 5-Column matrix /25 keys (interrupt driven)
      1 LCD-controller 8-bit parallel I/F @13MHz
        6800 or 8080 protocol
        DMA capability
      1 Multi-Channel Serial Interface @13Mbps
        Exclusive Static sharing DSP/MCU with DMA capability
        Voice Interface for external BlueTooth PCM-Codec connection
        cDSP sub-system debug…
LOCOSTO-IC DBB External I/F’s (1/4)

## Slide 16
  RHEA Bus (MCU &/ cDSP) @52Mhz (Continued)
    1 UART Modem/IRDA, Auto-Baud capability @115.2Kbps
      Exclusive Static sharing DSP/MCU with DMA capability
      Data Interface for external BlueTooth Modem connection
      Or Host serial cable (support Manufacturing Flash Loader @3.25Mbps)
      Or IRDA up to FIR @4Mbps
    1 I2C H/W-controller @400Kbps (MCU only) for controlling optional implementation such as:
      A-GPS module
      Frequency Modulation Radio chip(FM Stereo Radio)
      Camera Sensor/Module
      B/W LCD…
    2 I2C H/W-controller @400Kbps (1 MCU + 1 DSP /same bus I/F)
    1 USIM (Universal Subscriber Identity Module) Interface @100Kbps
LOCOSTO-IC DBB External I/F’s (2/4)

## Slide 17
  RHEA Bus (MCU &/ cDSP) @52Mhz (Continued)
      1 C-port/I2S Audio-Stereo Codec serial interface,
      Slave up to 3.072Mbps
      1 USB 1.1 client full speed (12Mbps)
        Host serial cable (PC connection…)
        Car-kit
        Battery charger
      Up to 48General Purpose I/O’s with Interrupt capability
LOCOSTO-IC DBB External I/F’s (3/4)

## Slide 18
Peripheral Bus (MCU)
  1 Parallel Camera-port
    Camera module (RGB & YUV output format)
  1 Nand-Flash 8-bit I/F up to 26MHz intended for Data storage.
  1 Master/Slave SPI up to 26Mbps with DMA capability
cDSP embedded TI Bus
  1 Voice Serial Port Slave @500kbps (DSP sub-system)
LOCOSTO-IC DBB External I/F’s (4/4)

## Slide 19: LOCOSTO-IC DBB SECURITY
  IMIF Bus (MCU)
      64-KByte Boot ROM,
      512-Byte Secure RAM
  Peripheral Bus (MCU)
      Protected Mode control & status register
      Random Number Generator
      Hashing SHA-1/MD5 Crypto-processor
      Symmetrical encryption DES/3-DES Crypto-processor
  RHEA Bus (MCU)
      Secure Interrupt Handler
      Secure Watch-Dog/Timer
      Protected Resources Reset Manager
      Enhanced Memory Protection Unit
      DMA’s secure-Channel
      CLKM; system-Clock’s Lock
      Manufacturer Public Key

## Slide 20: LOCOSTO-IC Engine Performance
DSP Sub-System @104Mhz
  c54x CPU based
  30-K 16-bit word RAM (including 16-Kw API)
  154-K 16-bit word ROM
  10-K 16-bit word RAM (external to cDSP; Patch, MP3…)
  Memory-mapped control & status register (XIO/RHEA @52MHz)

## Slide 21: LOCOSTO-IC Engine Performance
ARM7 @104Mhz, (Host processor)
  2.5-Mbit SRAM, single-cycle access @104MHz
  1.5-Mbit ROM (Midi, JPEG… ) single-cycle access @104MHz
  16-Kw ARM/cDSP RAM I/F (API), 2-cycle @104Mhz
  Memory-mapped control & status register
    RHEA @52MHz
    “Memory-Like” Peripherals @52MHz
  External memory extension Burst @52MHz

## Slide 22
LOCOSTO-IC Architecture Performances
DMA Subsystem
RAM
NOR
Flash
52 Mhz
104 Mhz
CPU (ARM7 TDMIE)
Subsystem
104 Mhz
16
CDSP M30L154
Subsystem
DARAM
PDROM
HWA
Video
API
16 K words
PROM
ROM
8*16 bits
Boot ROM
64 Kbyte
SRAM
2.5Mbit
104 Mhz
Des/3Des
Sha1/Md5
RNG
SPI
CAM/CCP
Nand-Flash
IMIF bus
52Mhz
32
EMIF bus
IMIF
Peripheralbus
32
52 Mhz
MCSI
UART
CPORT
16
ARM Rhea bus
Rhea Switch
OCP T1
DRP’S IF
USB
LCD
2 I2C
USIM
DRP’S IF
A5-1/2/3
16
52 Mhz
LOCOSTO
architecture
52 Mhz
16
API bus
ROM
1.5Mbit

## Slide 23: LOCOSTO-IC ARMIF
LOCOSTO-IC ARMIF
ARM MEMORY INTERFACE
TI proprietary Information, under Non-Disclosure Agreement

## Slide 24: LOCOSTO-IC ARMIF
The Arm memory interface handles
  Internal Arm memory access management
  Internal Arm peripheral access management
  External Arm Memory interface (EMIF) access management
  Arm to API memory access management
  Arm to Rhea bridge access management
  Arm nWAIT and access control flags generation
The Arm memory interface does not perform external memory decode anymore and depends upon the EMIF module to manage the external accesses

## Slide 25: LOCOSTO-IC EMIF
LOCOSTO-IC EMIF
EXTERNAL MEMORY INTERFACE
TI proprietary Information, under Non-Disclosure Agreement

## Slide 26: EMIF Block Diagram
The External Memory Interface (EMIF), is part of MCU sub-system that manages the read/writes between MCU/DMA and external memory (like flashes and SRAMs).
CONTROL & CONFIGURATION
REGISTERS
16
DMA BUS
32
MCU BUS
MCU BUS
INTERFACE
32
E
M
I
F
Prefetch
buffer
INTERFACE
DMA CTRL

## Slide 27: EMIF Features
Support 8/16/32 bit read/write from MCU/DMA
Burst read/write from DMA.
16-bit word data-bus
Supports up to 4 chip selects, each chip 32Mbyte
Each CS separately configurable for
  Asynchronous Read/Write (Default)
    Programmable Wait-States
    Support dynamic access time through external nRDY signal
  Synchronous Burst Read/Write
    Continuous, 4-, 8- 16 word burst
    52Mhz clock for burst accesses
Support wait state insertion for read and write access
External memory frequency configuration
Protect mode support (Read only)
Support only little endian format.

## Slide 28: EMIF External signals

## Slide 29: EMIF Multiplexed bus Address/Data

## Slide 30: EMIF Protocol mode
Different modes available through MEMMODE field of EMIF chip select configuration registers

## Slide 31: EMIF Handshaking mode
EMIF support the ready/Wait signal from the external memory in two modes. Assertion of ready/wait signal extend the access time until the ready/wait is de-asserted.
Non-full handshaking mode
  In this mode of operation the ready/wait signal from the memory is ignored.
Full handshaking mode
In this mode of operation the ready/signal from external memory extend the access time. In this there are two modes of support.

## Slide 32: EMIF Power Save Mode
EMIF supports two power saving modes:
  Global IDLE mode
  Dynamic power saving mode
Power saving modes depend on the:
  PDE
  PWD_en
  bit fields of EMIF configuration register
Notes: In dynamic power saving mode, EMIF slow is in idle mode when there are no
requests to it. The clock to EMIF Slow is disabled and EMIFS goes into idle mode.
In idle mode, the clock source sends the idle request to EMIFS to set it in idle
mode. In return, the EMIFS sends an acknowledge signal to the clock source
to set the idle mode after completion of the present request.
In dynamic power-saving mode, EMIFS is in idle mode when there are no requests
to it. The clock to EMIFS is disabled and EMIFS goes to idle mode.
EMIFS comes out of idle mode when there is a request from an initiator. This
mode can be enabled by setting the PWD_EN of the EMIFS configuration register
(EMIFS_CONFIG[2]). When this bit is set, EMIFS itself cuts the clocks,
providing there are no requests from the hosts through autogating clocks. The
power-saving modes depend on the PDE and PWD_EN bit fields of the EMIFS
configuration register (EMIFS_CONFIG[3] and EMIFS_CONFIG[2], respectively).
Table 9−38 lists the modes of operation when these bit fields are set.
PDE Global power down enable signal.
PWD_ENEMIF power down enable.

## Slide 33: LOCOSTO-IC DMA
LOCOSTO-IC DMA
TI proprietary Information, under Non-Disclosure Agreement

## Slide 34: DMA Features
6 channels
  Channel allocation ARM or DSP
  Secured channel configurable
4 ports
  RHEA
  API
  IMIF
  EMIF
2 levels of priority on each channel.
Both hardware / software request capability.
Transfer of data up to 32 bits.
Data burst capability.
Data packing / splitting.

## Slide 35: DMA Features
Data bursting.
3 addressing modes
  constant,
  post-increment
  frame-indexed.
Auto-initialization capability.
Auto Gating capability
Generation of interrupts on various events.
  End of block
  End of frame
  Half block
  Request drop
  Timeout
An element
  can be 1,2 and 4 bytes, programmable
A frame
  can contain 1~65535 elements, programmable
A block
  can contain 1~65535 frames, programmable
Notes: Constant addressing mode
  Used to point a peripheral that has fixed read/write address
  Address remains constant: A(n+1) = A(n)
Post-incremented addressing mode
  Used to point continuous memory addresses for data up/down loads
  A(n+1) = A(n) + ES

## Slide 36: DMA Channel Mapping
Note:
TX means data transfer from DMA to Peripheral
RX means data transfer from Peripheral to DMA

## Slide 37: Basic flow of DMA transfer

## Slide 38: LOCOSTO-IC CLOCK MANAGEMENT
LOCOSTO-IC CLKM
CLOCK MANAGEMENT
TI proprietary Information, under Non-Disclosure Agreement

## Slide 39: CLOCK MANAGEMENT
The Clock-Management system:
  DPLL
  CLKM
  APLL
Each associated to memory-mapped registers for programming DBB system clocks frequencies (DSP, MCU, Rhea-Bridge & Peripherals clocks).

## Slide 40: CLOCK MANAGEMENT OVERVIEW
Triton Lite
Locosto
DRP
DPLL
APLL
CLKM
32KHz
CLK_EN
1
3
M
H
z
(
N
R
)
1
0
4
M
H
z
(
N
R
)
104MHz(R)
1
3
M
H
z
(
R
)
DBB
NR - Non Retimed/Regenerated
R - Retimed/Regenerated
ULPD
Wakeup Req
Periph.

## Slide 41: CLOCK MANAGEMENT OVERVIEW
Locosto DBB has primarily four independent clock domains and many more derived clock domains.
The primary clock domains are:
  32KHz clock from Triton Lite
  13MHz clock from DRP
  104MHz clock from DPLL
  48 MHz clock from APLL

## Slide 42
To reduce the digital switching noise, MCU/DSP 104MHz clock also needs to be synchronous to the RF clock (ADPLL clock).
DPLL block uses the DRP non-retimed 13MHz clock to generate the 104MHz. This 104MHz from DPLL is only used by ULPD (for gauging).
MCU/DSP don’t directly use this clock but use a regenerated version of this clock.
DSP/MCU Clock Regeneration

## Slide 43: CLOCK MANAGEMENT DPLL
The DPLL is programmable in "multiplication-mode" with the following values:
m = 1 up-to 32 (step 1) d = 1, 2, 3 or 4
And in "division-Mode" with the following values:
k = 1, 2 or 4

## Slide 44: CLKM CLOCK TREE
CLKM
0
1
ARM domain
104 MHz clock
Divide by 2
ARM domain
52 MHz clock
Rhea, API bridge, Memory like peripherals
ARM Sleep
request
0
1
Bridge domain
104 MHz clock
DMA, Internal memory, EMIF
Divide by 2
Rest of
Bridge domain
52 MHz clock
DPLL Idle
request
External Clock
0
1
CNTL_ARM_CLK(1)
0
1
Bridge Sleep
request
104MHz
Regenerated
DSP domain
104 MHz clock
Divide by 2
DSP domain
52 MHz clock
IDLEN from
cDSP
SYS Clock
Tmer, TPU…
DPLL
RESYNCH / DPLL
13M
RESYNCH / 13M

## Slide 45: PERIPHERALS CLOCK TREE
APLL
48 Mhz/
24 Mhz/
3 Mhz
13MHz NONE
RESYNCH
52 Mhz generated
from bridge clock
Camera clock
DCXO source
(13 Mhz)
52 Mhz generated
from bridge clock
UART/ MSSPI clock
USB clock
This clock is not used for RX/TX USB, it’s used only for CPU access
DCXO source (13 Mhz)
52 Mhz
ARM clock
RX/TX USB clock
48MHz

## Slide 46: LOCOSTO-IC LCD INTERFACE
LOCOSTO-IC
LCD INTERFACE
TI proprietary Information, under Non-Disclosure Agreement

## Slide 47: LCD INTERFACE FEATURES
8-bit parallel Interface
Compliant 6800/8086 .
Can interface two external LCD (2 Chips select)
Compliant for QCIF (176x144) /QVGA (160x120) resolution.
The maximum transfer rate is 13Mbytes per seconds.
DMA management

## Slide 48: LCD INTERFACE OVERVIEW
RHEA I/F
Registers
Received data register
Transmit FIFO
(128x16)
State Machine
RS
nCS
Data_out
Data_in
RnW
ESTRB
Clock management
RHEA bus
nIRQ
Clock 13MHz
RHEA I/F
Registers
Received data register
Transmit FIFO
(128x16)
State Machine
RS
nCS0,1
Data_out
Data_in
RnW
ESTRB
Clock management
RHEA bus
nIRQ
Clock 13MHz

## Slide 49: LCD INTERFACE SIGNALS

## Slide 50: LOCOSTO-IC NAND FLASH INTERFACE
LOCOSTO-IC
NAND FLASH
INTERFACE
TI proprietary Information, under Non-Disclosure Agreement

## Slide 51: NAND FLASH INTERFACE FEATURES
Flexible architecture to support different sizes of Nand Flash Memory
8-bit data (commands, addresses and data are multiplexed) and 8 bits control interface to Nand Flash Memory
8, 16 and 32 bits interface from host processor to buffer, 32 bits for registers.
Double page Buffer implementation (2*128 bytes)
Programmable Nand Flash access time
Interrupt and flag (polling operations) for end page, end transfer, end ECC and end busy
Fully automatic transfer process
Programmable number of bytes for command, address and data
Support different page size of Nand Flash Memory
Low consumption in idle
Support DMA transfer and DMA request
Support sequential read in Nand Flash Memory
Support Error Code Correction (ECC)

## Slide 52: NANDFLASH INTERFACE BLOCK DIAGRAM

## Slide 53: NAND FLASH INTERFACE SIGNALS

## Slide 54: LOCOSTO-IC CAMERA APPLICATION
LOCOSTO-IC
CAMERA APPLICATION
TI proprietary Information, under Non-Disclosure Agreement

## Slide 55: CAMERA FLOW

## Slide 56: CAMERA USE
Preview mode: in this mode, the current view is displayed on the LCD, so that the user can adjust its position. The display is refreshed at 15 fps.
Snapshot mode: in this mode, the current picture is captured into RAM. It is then compressed into JPEG format and sent to an appropriate storage device (e.g. flash RAM).

## Slide 57: SYSTEM REQUIREMENTS
Camera and LCD RGB data format (used during viewfinder) must match, and integrate properly with the existing graphics software.
I/O voltage: Locosto I/O voltage is 1.8V.
Viewfinder frame rate of no less than 15 fps is targeted.
Total time for snapshot capture to memory must be less than 1/5 s.
Total “shot to shot” delay must be less than 5 s.

## Slide 58: CAMERA SYSTEM IMPROVEMENT
Double the frequency of the CPU from 52 MHz to 104 MHz, to increase performances
Add a DMA to external memory, to diminish the impact of the increased external RAM bandwidth usage on the CPU load
Use Read/Write burst RAM, to maintain acceptable external RAM throughput
Add a prefetch buffer for CPU code fetches, to maintain acceptable performances when fetching code from external RAM
Embed some software engines (MIDI and JPEG) in an internal ROM. This makes it possible to benefit from fast, 32bit accesses for those CPU demanding routines, while accounting for only ¼ of the equivalent RAM size on the silicon

## Slide 59: CAMERA HARDWARE SYSTEM DIAGRAM
8bit
@12MHz
“Dispatched”
Bus
Cam
DMA
ARM7
ROM
/SRAM
RAM
Flash
Camera
VGA & QCIF
RGB & YUV
LoCosto
System external memory
LCD
QCIF /+
LCD
I/F
8-bit @6.5MHz
I2C
Control
16bit @52MHz
32bit @104MHz
16bit @52MHz
32bit @52MHz
“Shared” Bus

## Slide 60: CAMERA SYSTEM ARCHITECTURE
(Engine ROM’ed 20KB ~30%)
LCD
(QCIF, 64k colors)
Display F-Buffer: 50 Kbytes
RGB-565 (16bit/pixel)
Mass Storage device
External E-RAM #1
External E-RAM #3
Snapshot F-Buffer: 600 Kbytes
YUV422 (16bit/pixel)
JPEG F-Buffer: 60 Kbytes
JPEG image
View
Finder & Display
CMOS Sensor
(VGA
&
QCIF)
QCIF
VGA
Image
Capture & Play
YUV422
(16bit/pixel)
Image capture
DMA Burst write 600 kbytes Block
(1 s/w ISR)
JPEG
Co-Dec
Sensor, DMA & Bus Mux‘ing Control
Camera Core
600-kB
8 bits /70ns
42ms + I/Line
Typ 200ms
Camera Core
Image capture
DMA Burst write 50 Kbytes Block
(1 s/w ISR)
RGB565 (16bit/pixel)
50-kB
8 bits /70ns
3.5ms + I/Line
Typ 15ms
External E-RAM #2
16 bits / ~25ns
Image Storage
Image Load
(FFS s/w)
Image Display
DMA Burst write 50 kbytes Block
(1 s/w ISR)
50-kB
8 bits /140ns
8 ms
LCD I/F
60-kB
8 bits /100ns ~6 ms
+ Progr Time (storage)
Downscaling & YUV to RGB conversion
16 bits / ~25ns

## Slide 61: CAMERA REQUIREMENTS
Picture size: The camera module must be able to deliver pictures in the range QCIF / 176x144 up to VGA / 640x480.
Frame rate: The targeted frame rate in viewfinder mode is 15 fps.
Data format: The output formats that need to be supported natively by the camera module are the following:
  RGB888 and/or RGB565
  YUV 4:2:2
Data interface: an 8 bit parallel data interface is used when the camera is connected directly to Locosto. The frequency depends on the picture size, but is limited to 48 MHz.
Tristate capability (according to pin mux configuration).
Control interface: the control commands will be send through I2C in the case of a directly connected parallel camera.
I/O voltage:1.8 V. In case of 2.8V I/O camera module is to use external level shifters on the board.

## Slide 62: LCD REQUIREMENTS
LCD size: a typical LCD for the camera application will be QCIF / QCIF+ (i.e. 220x170 pixels).
Data format: the LCD needs to accept data in RGB565 (two bytes) format and/or RGB888 (three bytes) format.
LCD Interface: Locosto comprises an 8 bit large LCD interface, that can run at a fraction of 13 MHz in {1, 2, 4, 8}.
I/O voltage: due to Locosto C027 process, Locosto LCD interface’s I/O support 1.8V. The LCD component has to support 1.8V I/O for proper connection.

## Slide 63: LOCOSTO-IC EXTERNAL PERIPHERALS
LOCOSTO-IC EXTERNAL PERIPHERALS
Keyboard
MCSI
UART
I2C
USIM
C-PORT
USB
TI proprietary Information, under Non-Disclosure Agreement

## Slide 64
EXTERNAL I/F BLOCK DIAGRAM
VSP
Voice Link
4
USIM

## Slide 65: LOCOSTO-IC EXTERNAL PERIPHERALS
SCANNED KEYBOARD
TI proprietary Information, under Non-Disclosure Agreement

## Slide 66: SCANNED KEYBOARD DIAGRAM

## Slide 67: SCANNED KEYBOARD FEATURES
Works on 32kHz main clocks
Debouncing time programmable
Support of multi-configurations keyboard, up to 8 columns * 8 rows. But Locosto is only 5*5.
Multi keys press detection and decoding (2 keys fully compliant but more than 2 with some limitations).
Each ARM interrupt enabled or disabled by register configuration.
Module generates an overrun if CPU reads register to late.
Interrupts generated on level
Each key coded on one bit in four 16 bits registers.

## Slide 68: LOCOSTO-IC EXTERNAL PERIPHERALS
MCSI (Multi-Channel Serial Interface)
TI proprietary Information, under Non-Disclosure Agreement

## Slide 69: MCSI FEATURES
Serial Interface with a Multi-Channels transmission capability.
Support the audio link with an external Bluetooth baseband IC device.
All transmission parameters are configurable to cover the maximum number of operating conditions:
  MASTER or SLAVE clock control (transmission clock and frame synchronization pulse)
  Programmable transmission clock frequency from 5KHz to 6MHz (Reference clock 13MHz)
  Single (1 channel per frame) or Multi (x16) channels frame structure
  Programmable word length : 3 to 16 bits
  Full-duplex transmission
  Programmable frame configuration
  Programmable interrupts occurrence time (TX and RX)
  Error detection with interrupt generation on wrong frame length
Support of GSM DAI operating modes.
Notes:   Programmable frame configuration
    Continuous or burst transmission
    Normal or Alternate framing
    Normal or inverted frame polarity
    Short or long frame synchro pulse
    Programmable over-size frame length
    Programmable frame length

## Slide 70: LOCOSTO-IC EXTERNAL PERIPHERALS
UART Modem / IrDA
TI proprietary Information, under Non-Disclosure Agreement

## Slide 71: UART MODEM / IRDA BLOCK DIAGRAM

## Slide 72: UART MODEM / IRDA FEATURES
UART Modem Functions
  Baud-rate from 300 bits/s up to 3.6864 Mbits/s
  Auto-baud between 1200 bits/s and 115.2 Kbits/s
  Software/Hardware flow control
  Programmable serial interface characteristics
IrDA Functions
  Slow infrared (SIR up to 115.2 KBAUD)
  medium infrared (MIR 0.576 MBAUD & 1.152MBAUD)
  fast infrared (FIR 4.0 MBAUD) operations (very fast infrared (VFIR) is not supported)

## Slide 73: LOCOSTO-IC EXTERNAL PERIPHERALS
I2C
TI proprietary Information, under Non-Disclosure Agreement

## Slide 74: MULTI-MASTER I2C
Main features of the I2C controller are:
  Compliant to Philips I2C specification version 2.1
  Standard (100 Kbits/s) and fast modes (400 Kbits/s)
  7-bit and 10-bit device addressing modes
  H/W asserted Start/Stop conditions, Ack/Nack; S/W control for Repeated-Start
  Multi-master Arbitration & clock synchronization
  Built-in FIFO for buffered read or write; 2 x 16-bit word
  16-bit wide access to maximize bus throughput
  Module enable/disable capability
  Programmable clock generation
  Two DMA channels:
    Receive-channel: Synchronously reads received data into the FIFO
    Transmit-channel: Writes data to be transmitted into the FIFO
  Six interrupt sources, grouped to one CPU’s IRQ-line

## Slide 75: MULTI-MASTER I2C BUS
MCU top
RHEA
BRIDGE
XIO
-
RHEA
cDSP sub
I2C
-
Triton Lite
I2C
-
Triton Lite
2
2
I2C Triton Lite I2C GP
I2C-GP
LOCOSTO-IC
I2C-TriTon Lite for controlling
  TriTon Lite-ABB
    from the DSP (Voice, Stereo-Audio)
    from the MCU (LDO’s, MADC, RTC…)
  Additional Slave-only components.
I2C-GP for multi-master system.

## Slide 76: I2C TRITON Lite BUS
LOCOSTO-IC

## Slide 77: EXTERNAL PERIPHERALS
USIM INTERFACE (Universal Subscriber Identity Module)
TI proprietary Information, under Non-Disclosure Agreement

## Slide 78: USIM
Designed to support many simultaneous smart-card applications such as SIM (GSM), USIM (3GPP), banking (EMV) and loyalty application.
Implements:
  the hardware interfaces to the Smart Card
  a sequencer that manages the transmission protocols T-0 and T-1, defined in the ISO7816.3 standard, thus freeing the MCU of the real-time constraints.
7
6
5
4
3
2
1
I/O
CLK
RST
card detection
8
CD
SIM Card
Controller
SIM Card
Controller
Port 1

## Slide 79: USIM BLOCK DIAGRAM
CARD PRESENCE DETECTION is done in TRITON Lite.
RHEA
INTERFACE
REGISTER
BLOCK
CLOCK
MODULE
SEQUENCER
INTERRUPT
CONTROLLER
SYNCHRO-
NIZATION
MECHANISM
DMA
INTERFACE
TX/RX BLOCK
TRANSMITTER
RECEIVER
TX FIFO
16-bytes
RX FIFO
16-bytes
13MHz
RHEA
BUS
SIM
CARD

## Slide 80: EXTERNAL PERIPHERALS
C-PORT (Codec Port Interface)
TI proprietary Information, under Non-Disclosure Agreement

## Slide 81: C-PORT

## Slide 82: C-PORT

## Slide 83: EXTERNAL PERIPHERALS
USB
TI proprietary Information, under Non-Disclosure Agreement

## Slide 84: USB FEATURES
USB_W2FC module: USB 1.1 client full speed (12Mbps)
Interface between the MCU and the USB device and handles USB transactions with minimal MCU intervention
Requires a 48MHz clock generated by APLL upon request
Locosto chip does not integrate the transceiver (differential drivers) that are available in TriTon Lite ABB chip; the USB_W2FC interface is supplied at 1.8v.
2 USB Modes
  DAT_SE0 for single-ended transactions with the USB controller (DBB chip) (3-pins),
  VP_VM for differential communications with the USB controller (4-pins).

## Slide 85: USB CONNECTIONS
MCU USB I/F: 4 pins – VDDIO power domain (1v8) – Multiplexed with UART |  | 
USB_RCV | IN | USB Differential Receiver input; not used in 3 pins DAT_SE0 mode.
USB_SE0_VM | IN/OUT | - USB SE0 in 3 pins bi-dir DAT_SE0 mode
 |  | - VM function in 4 pins bi-dir VP_VM mode
USB_DAT_VP | IN/OUT | - DAT function in 3 pins bi-dir DAT_SE0 mode
 |  | - VP function in 4 pins bi-dir VP_VM mode
USB_TXEN | OUT | USB Transmit Enable
TRITON Lite USB Transceiver
USB_TXEN
USB_DAT_VP
USB_RCV
USB_SE0_VM
LOCOSTO DBB
OE
DAT_VP_RXD
RCV
SE0_VM_TXD
TRITON Lite
USB W2FC (Client only)
USB-Xcvr
DP_RX_MIC_R
DM_TX_SPK_L
VBUS

## Slide 86: SECURE ENVIRONMENT
SECURE ENVIRONMENT
Secure hardware
PRRM (Protected Resource Reset Management)
Cryptography
EMPU (Enhanced Memory Protection Unit)
TI proprietary Information, under Non-Disclosure Agreement

## Slide 87: GENERAL INTRODUCTION ON SECURITY
What do we try to achieve with a secure system?
Protection against firmware Modification
Secure Download of the firmware
Protection Against Cloning Between Mobile
Secure Confidential Data Encryption/Decryption
Protection Against Reverse Engineering

## Slide 88: SECURE ENVIRONMENT ARCHITECTURE

## Slide 89: SECURE ENVIRONMENT
SECURE HARDWARE
TI proprietary Information, under Non-Disclosure Agreement

## Slide 90: SECURE HARDWARE
  64Kbyte secure boot ROM
  512byte secure RAM
  16-bit protected mode control
      and status register (PMCTLST register).
  Secure Access Controller

## Slide 91: SECURE BOOT ROM (Overview)
Content (64kBytes):
Secure ROM content cannot be read/dumped
Any access to the secure code from outside the Secure-ROM or in emulation is denied.
It cannot be interrupted or bypassed.
It is not dependant on the OS.

## Slide 92: SECURE RAM
512 bytes (128x32-bit)
Dedicated SRAM used for secure context stack operations and short data/variables storage.
DMA accesses are not serviced.
Reserved for secure-ROM code execution
Any access from outside the Secure-ROM code or in emulation is denied.
Its content is cleared upon reset event

## Slide 93: SECURE ENVIRONMENT
PRRM
Protected Resource Reset Management
TI proprietary Information, under Non-Disclosure Agreement

## Slide 94: PRRM

## Slide 95: PRRM FEATURES
The PRRM - “reset module” - can perform a reset on:
    the internal memory space,
    the API memory space,
    the protected resources (Secure RAM, RNG, DES, 3DES, …).
It also can generate:
    a Global chip reset,
    a protected resource reset,
    an opcode prefetch abort.
The PRRM reset is initiated on different reset sources:
    Global chip reset request,
    Protected resource reset request,
    Secure watchdog timer reset request,
    Soft reset.
1/2

## Slide 96: SECURE ENVIRONMENT
EMPU
Enhanced Memory Protection Unit

## Slide 97: EMPU

## Slide 98: EMPU

## Slide 99: EMPU FEATURES
The EMPU allows defining internal-memory sub-regions, each having a separate protection attribute.
This permits for partitioning the memory space into program instruction, system data, user data, stack …
The address bus directly issued from the processor is monitored providing a real-time position of the memory region accessed. When a protection breach attempt occurs:
    the memory control signals are affected,
    no writing/reading into/from the memory,
    and the fault condition is indicated to the processor.
The EMPU allows for controlling 3 different protected memory spaces shared by a Micro-controller and a Direct Memory Access (DMA):
    API memory space,
    External memory space,
    Internal memory space.

## Slide 100: EMPU INTERNAL MEMORY
  Up to 4 programmable protected regions within a maximum memory space of 256 k-byte
  A 64 k-byte maximum region size (256 k-byte for 4 regions).
  A minimum granularity of 8 bytes (minimum protected region size)
  4 protection modes applied to the memory sub-region bounded by the starting/ending addresses:
      Non-User R/W,
      User Read-only,
      ROM,
      Privileged-region write
  Definition by region base address and starting/ending addresses within the protected memory region

## Slide 101: EMPU API
  2 regions, programmable boundary API protected region
  A minimum granularity of 1 byte on the API
  3 protection modes:
      Read protect,
      Write Protect,
      Read/Write protect
Protected region 2
Protected region 1
API Bound Address
API memory

## Slide 102: EMPU EXTERNAL MEMORY
  The protected region from the External memory base address within the system memory map to the limit of this region.
  A minimum granularity of 128 bytes on external memory
  Protection Mode enabled/disabled (protection type is internally hard coded to protected write)
  The protection enable bit is “write once” and is activated according to the External memory chip select defined in the control register. This feature allows protecting an external memory in any chip select configuration.
Unprotected region
Protected region
EXT Boundary Address
External memory

## Slide 103: EMPU
The EMPU generates:
  An illegal-access signal for each type of protected memory space (internal, external and API) if the application program attempts a non-authorized access to a memory region (i.e. User write access to a region programmed for User Read-only accesses).
  A MPU-fault signal which is a logical function of the 3 protected spaces (internal, external and API) Illegal-access signals.
  A fault indication (Illegal-access) flagged into the EMPU status register which is available to the processor for fault analyze.

## Slide 104: LOCOSTO-IC SECURE BOOT
LOCOSTO
VS
CALYPSO PLUS

## Slide 105: HW DIFFERENCES
Boot ROM size is now 64 KB as compared to 48 KB in Calypso plus.
Only One UART Module in Locosto.
USB Transceiver resides in Triton Lite
Internal SRAM is reduced to 2.5 M-bit (320KB); Hence for flash programmer code, effectively only 1 M-bit of SRAM will be available (128 KB)
Die-ID size is increased to 128 bits
EMIF has changed from Calypso Plus – Permitting to have a maximum of 4 chip selects (CS0/1/2/3) with a maximum of 32 MB each. Also Burst mode access to external memory is added and Page mode access is removed.
MCU Clock frequency in Locosto can go up to 104 MHz.

## Slide 106
THANK YOU!