## Slide 1
Locosto DRP
David-wang@ti.com

## Slide 2: Locosto DRP
DRP2.0 Overview
Receiver
LO, Synthesis and Transmitter
DCXO
DRP LDOs and Power Management
APC
AGC
Clock management
Script Processor and SRM
DRP Wrapper
DRP Timings

## Slide 3
Digital RF Processor
Overview

## Slide 4: DRP summary
Locosto DRP is a fully integrated 4 band GPS/GPRS transmitter
The DRP technology enables software definable radio (SDR)
This technology allows cost effective integration of the radio function
TI Digital Radio Processor (DRP) is a complete Radio subsystem including:
  Frequency synthesizer: ADPLL
    Digitally Controlled Oscillator (DCO)
    Digital loop filter and phase detector
    Reduced Lock Time (Loop BW adaptation)
  Transmitter:
    Based on ADPLL
    Digitally self-calibrated two-point modulation
  Receiver:
    Configurable to zero IF or near zero IF
    MTDSM (multi-tap-direct-sampling-mixer)
    LO generated by ADPLL
  Digital Interface with Baseband
  Power management and start up engine (On-chip Bandgap + LDOs)
  Clock management (DCXO) with clock noise reduction by retiming
  Software script processor for transceiver sequencing and calibration

## Slide 5: Radio Interface Block Diagram
AFE
ABE
ADPLL

## Slide 6
Digital RF Processor
Receiver

## Slide 7
RX Location in DRP2 system
PPA_LB
SAM
PPA_HB
LDOOSC
TDC
DCO
OSC
LDOX
DIG
DRP
ANA
ALOTX
DCXO
DLO
DTX
FLT
INTPL
PHASE
DCOIF
CAL
CTL
SRM
FREF
MEM
DRX
O
C
P
MEM
D
T
S
T
SCR
MEM
JTAGIF
DMUX
RFTST
MEM
SW
FCU
I/Q
DACs
LUT
PRE
DCEST
R
C
F
1
P
R
E
F
I
Q
M
C
R
E
S
R
O
C
C
S
F
Z
I
F
from DTX
MEM
DCXOIF
CKR
FREF
LF
CKRET
(CKRET
PVL)
Note: The DRX path is
time interleaved
USD
CKV
BGAP
LOCOSTO
WRAPPER
RAM
TXBUF
RXBUF
SCRMEM
ARXCWIF
DCU
SCF
FBUF
AFE
C
H
Q
ARXCW
PCS
DCS
EGSM
GSM
MTDSM
SCF
FBUF
PCU
ATST
A
D
C
CTA
LDOA
SDM
IREF GEN
ADC
REF
ABE
A
D
C
LUT
POST
CTA
SDM
ADC
REF
M
I
X
H
B
T
A
H
B
L
N
A
H
B
M
I
X
L
B
T
A
L
B
L
N
A
L
B
/2
/2
/4
/2
SDM
IDAC
SUS
PDET
ADC
AMPLITUDE
CONTROL
XTAL_CTL
GSM/
EGSM
DCS/
PCS
CKM
CKM
LDORF
SLEEPX
F32
PURX
VCORE
VR1
VR2
(BGAP & LDOX)
1.4V, 30mA
1.4V, 30mA
1.4V, 30mA
1.4V, 5mA
(1.35V)
(2.78V)
(2.78V)
TSP
BSP
BRIDGE
VBUF
TEMPSENS
BUFFER
C
H
I
I-Channel
Q-Channel
XTAL

## Slide 8: RX blocks
IREFGEN

## Slide 9
Digital RF Processor
LO & Synthesis
& Transmitter

## Slide 10: DRP2.0 SYNTHESIZER/TX BLOCK DIAGRAM
TRF6151 building blocks | DRP “equivalent”
VCO (voltage controlled oscillated | DCO (Digitally-Controlled Oscillator )
PFD (Phase frequency detector) and CP (charge pumps) | Digital comparator + Time-to-Digital Converter (TDC)
Loop filter | Digital Loop Filter (LF)
Analog TX buffers | programmable pre-power amplifier (DPA)
ADPLL
MAIN VCO 1 @ 3.37 GHz
MAIN VCO 2 @ 3.80 GHz
TX LB VCO
TX HB VCO
toward RX mixers
IF filter
Main Loop Filter
26 MHz
PFD
R
N
L
M
PFD
PAD
90o
IF
LO
Q
I
MAIN PLL

## Slide 11: Frequency synthesizer
Based on an All-Digital PLL (ADPLL)
  Digitally Controlled Oscillator (DCO) at 1.8 GHz as the RF frequency source
  The frequency setting uses FCW (fixed-point Frequency Command Word)
  The phase correction mechanism in 2 steps:
    The integer part of the phase detector computes the phase difference between the DCO output clock and the retimed reference clock (reference clock resynchronized with the DCO clock)
    The fractional phase error between the reference and DCO output clocks is estimated by the TDC (Time to Digital Converter) and added to the integer phase error..
Notes: At last we have arrived at the big picture of the all-digital PLL architecture. All signals shown are digital. The ADPLL operates in the phase domain as follows. The rising-edge DCO transitions are counted by the variable phase accumulator. The frequency command word or the fractional-N frequency division ratio is accumulated in every FREF cycle by the reference phase accumulator. The sampled variable phase is subtracted from the reference phase by the fixed-point arithmetic phase detector. The phase error samples adjust the phase and frequency of the DCO in the negative feedback manner. The fine phase resolution is achieved by the time-to-digital converter, which measures the time difference between the DCO clock and FREF with the resolution of one inverter.

## Slide 12: All-Digital PLL (ADPLL) block diagram
Synchronous digital phase domains (key idea of the ADPLL to avoid metastability problems in TDC and reduce noise)
Notes: At last we have arrived at the big picture of the all-digital PLL architecture. All signals shown are digital. The ADPLL operates in the phase domain as follows. The rising-edge DCO transitions are counted by the variable phase accumulator. The frequency command word or the fractional-N frequency division ratio is accumulated in every FREF cycle by the reference phase accumulator. The sampled variable phase is subtracted from the reference phase by the fixed-point arithmetic phase detector. The phase error samples adjust the phase and frequency of the DCO in the negative feedback manner. The fine phase resolution is achieved by the time-to-digital converter, which measures the time difference between the DCO clock and FREF with the resolution of one inverter.

## Slide 13: Reference Phase Retiming
Within the ADPLL, DCO clock and FREF domains are not entirely synchronous despite being in phase lock
Solution: Oversampling FREF by CKV and using the resulting CKR
26 Mhz from DCXO
Retimed reference
Derivative from DCO output frequency (channel dependant)
Notes: The two clock domains, the variable DCO and the FREF, are not entirely synchronous. During the acquisition, their edge relationship is not known. During the PLL lock, they might exhibit phase rotation if the FCW is fractional-N. Under these circumstances, the digital circuitry cannot operate properly without facing metastability problems. Our solution was to create a single clock CKR that is synchronous to the DCO clock. This is done by oversampling the FREF by the high-speed DCO clock using a flip-flop. This operation is mathematically described as a numerical ceiling operation.

## Slide 14: All-Digital PLL (ADPLL) block diagram
Notes: At last we have arrived at the big picture of the all-digital PLL architecture. All signals shown are digital. The ADPLL operates in the phase domain as follows. The rising-edge DCO transitions are counted by the variable phase accumulator. The frequency command word or the fractional-N frequency division ratio is accumulated in every FREF cycle by the reference phase accumulator. The sampled variable phase is subtracted from the reference phase by the fixed-point arithmetic phase detector. The phase error samples adjust the phase and frequency of the DCO in the negative feedback manner. The fine phase resolution is achieved by the time-to-digital converter, which measures the time difference between the DCO clock and FREF with the resolution of one inverter.

## Slide 15: Gear-Shifting of PLL Bandwidth
Progressive reduction of ADPLL loop bandwidth while the loop is settling
Lock time max = 170 usec (RX) and 240usec (TX)

## Slide 16: ADPLL BUILDING BLOCKS (1/5)
Digitally-Controlled Oscillator (DCO) Time-to-Digital Converter (TDC) Digital Loop Filter (LF) All-Digital PLL (ADPLL) ADPLL Wideband Frequency Modulation

## Slide 17: DCO: varactor banks overview

## Slide 18
ADPLL BUILDING BLOCKS (2/5)
Digitally-Controlled Oscillator (DCO)
Time-to-Digital Converter (TDC)
Digital Loop Filter (LF)
All-Digital PLL (ADPLL)
ADPLL Wideband Frequency Modulation

## Slide 19: Time-to-digital Converter (TDC)
Estimates the fractional Phase Error
Quantized phase detector with resolution of <20 ps
Notes: Time difference between the rising edge of FREF and both rising and falling DCO edges is measured by the time-to-digital converter in units of the inverter delay. Since the TDC output is subject to PVT, it needs to be normalized to the DCO period before being fed into the loop.

## Slide 20
ADPLL BUILDING BLOCKS (3/5)
Digitally-Controlled Oscillator (DCO)
Time-to-Digital Converter (TDC)
Digital Loop Filter (LF)
All-Digital PLL (ADPLL)
ADPLL Wideband Frequency Modulation

## Slide 21: Digital loop filters
4th order digital IIR loop filter to suppress the frequency reference and TDC quantization noise
Unconditionally stable IIR filters
Single-pole IIR stage:

## Slide 22
ADPLL BUILDING BLOCKS (4/5)
Digitally-Controlled Oscillator (DCO)
Time-to-Digital Converter (TDC)
Digital Loop Filter (LF)
All-Digital PLL (ADPLL)
ADPLL Wideband Frequency Modulation

## Slide 23: All-Digital PLL (ADPLL)
Type-II 6th-order PLL loop
Reduced Lock Time (Loop BW adaptation)
Synchronous digital phase domains (key idea of the ADPLL to avoid metastability problems in TDC and reduce noise)
Notes: At last we have arrived at the big picture of the all-digital PLL architecture. All signals shown are digital. The ADPLL operates in the phase domain as follows. The rising-edge DCO transitions are counted by the variable phase accumulator. The frequency command word or the fractional-N frequency division ratio is accumulated in every FREF cycle by the reference phase accumulator. The sampled variable phase is subtracted from the reference phase by the fixed-point arithmetic phase detector. The phase error samples adjust the phase and frequency of the DCO in the negative feedback manner. The fine phase resolution is achieved by the time-to-digital converter, which measures the time difference between the DCO clock and FREF with the resolution of one inverter.

## Slide 24
ADPLL BUILDING BLOCKS (5/5)
Digitally-Controlled Oscillator (DCO)
Time-to-Digital Converter (TDC)
Digital Loop Filter (LF)
All-Digital PLL (ADPLL)
ADPLL Wideband Frequency Modulation

## Slide 25: ADPLL with GMSK Modulation
Two-point modulation
  Direct feedforward path : y[k] directly drives the DCO
  Compensating path: y[k] added to the channel FCW
Notes: The presented ADPLL features a wideband frequency modulation capability. The modulating samples are injected at two points in the ADPLL loop. The modulation method is similar to the conventional two-point modulation scheme, but here it is exact due to its digital implementation. The modulating samples y[k] directly affect the DCO frequency deviation. The delta f gets integrated in the variable accumulator but the PLL perceives this as a DCO noise. This is compensated by adding the modulating samples to the channel FCW. With this method, the loop dynamics are removed from the modulating path, while all the error sources still undergo the normal loop response.

## Slide 26
OTHER RF TX BUILDING BLOCK
Digitally-Controlled Power Amplifier

## Slide 27: Digitally-Controlled Power Amplifier
Class-E PA with MOS transistor switches
The DPA can be thought of as an RF DAC, where “A” is RF “amplitude”
Array of unit-weighted MOS switches, that can be programmed through API to achieve the TX desired output level (up to +8dBm)
Notes: The digital DCO output drives the NMOS transistors operating as digital switches, which are then terminated by a matching network. A single transistor switch in a conventional class-E power amplifier is replaced by a multitude of switches. The RF amplitude is digitally controlled by regulating the number of active switches. In this design we have achieved a 6-bit basic amplitude control.

## Slide 28
Digital RF Processor
DCXO

## Slide 29
AFC Loop in GSM/EDGE Network
Freq Sync Signal
0.1ppm freq accuracy
required (GSM/WCDMA)
I
Q
I
Q
Digital
Baseband
RF+ABB+DBB
PPA
LNA
Synthesizer
DAC
ADC
PA
T/R SW
0
90
0
90
Freq Sync
Signal
DCXO
26MHz REFCLK
TX Signal
< 0.1ppm
Freq Error
ADC
DAC

## Slide 30
VCXO vs. DCXO
XI
GND
DCXO
RF+ABB+DBB
Digital BaseBand
AFC
VCTRL
Trim
GND
VDD_HI_Volt
AFC DAC
AFC
RF+ABB+DBB
Digital BaseBand
VCXO
XI
DCXO

## Slide 31: DRP - DCXO overview
Low phase noise clock reference for RF clock synthesis
Large tuning range : 10 bits digital codeword for coarse tuning
Accurate frequency : 14 bits digital codeword for fine tuning
Oscillation amplitude control to limit crystal power drive
Oscillation amplitude detection to tune startup time
State machine for startup tuning procedure

## Slide 32: DCXO System
BGAP
LDOX
IDAC
Peak
Detect
ADC
IIR
IIR >
Thresh1
IIR >
Thresh2
Thresh1
Thresh2
Time
Measurer
Time
2
– Time
1
IDAC
INT
1
Time
Expected
Unity
Mult1
Mult2
State
Machine
OSC
SDM
FREF
F32
:
:
:
13:4
C
O
R
O
W
XTAL_CONTROL
1
DITHER
1
Amplitude Control
FREF (CKXA)
/16
Startup
State
Machine
VR2
4
Amplitude Control Block

## Slide 33: Coarse Frequency Control
Coarse Frequency Adjustment (CFA) capacitor consists of:
Fixed capacitor of size 168 units
Modified-binary array with 10-bit control, with individual weights of 1, 2, 3, 6, 12, 24, 48, 96, 192 and special capacitor of ~200 units respectively
CFA calibration is needed to obtain initial CFA value that gives optimal tuning range using Fine Frequency Adjustment only

## Slide 34: Fine Frequency Adjustment
Fine Frequency Adjustment (FFA) is controlled via 14-bit codeword
The physical capacitor array consist of 1024 capacitors.
Capacitor array is tapered, with sizes ranging from ~30fF to 100fF.
Tapering creates linear transfer function between codeword and the frequency
Additional 4 bits of frequency resolution are obtained via digital Sigma-Delta modulation of an array element
Notes: δf = ∆f / 2^10 => min 51.3 / 1024 = 0.05ppm / unit
0.05ppm / 2^4 (SD) => 0.003 ppm

## Slide 35: Fine Frequency Adjustment (cont.)
Example:
14-bit codeword, codeword 0000000010_0111, or 2 and 7/16th correspond to turning on 2 capacitor array elements, and turning on another capacitor element, 7 out of every 16 FREF clocks (on average)
Typical frequency resolution of the FFA is 0.002 to 0.003ppm/LSB
This may vary substantially with the crystal and CFA value chosen during calibration

## Slide 36: Amplitude Control in DCXO
High amplitude of oscillation in a DCXO produces superior phase noise
High amplitude of oscillation may cause power drive of crystal to be exceeded causing damage to the unit
The Amplitude is directly affected by the current
The Amplitude is also heavily influenced by the changes in tuning capacitance (FFA)

## Slide 37: DCXO Startup
DCXO startup and wakeup require special hardware, since FREF clock is not available until DCXO becomes fully operational and therefore the DSP, the Script Processor and the FLASH memory are inaccessible
DCXO startup is clocked by the clock from the 32kHz crystal
All three IDAC codewords go to their default values of
  Numerator = 128
  Denominator + Fraction + Fixed = 0 + .0 +128

## Slide 38: DCXO Startup
Startup sequence consists of three phases
Quick Charge: IDAC current is set to 3X nominal value of IDAC current. This is done in order to guarantee that the oscillations will begin. The output of the 5-bit ADC is monitored for the crossing of first programmable threshold (thr1). On the second 32 kHz clock cycle after the crossing of the thr1 is detected, Phase 1 ends.
Linear Ramp: IDAC current is set to X nominal value of IDAC. The output of the ADC is monitored for crossing of the second programmable threshold (thr2).
Final Settling : New value for IDACN is set using formula

## Slide 39: DCXO Startup (cont.)

## Slide 40
Digital RF Processor
Power Management

## Slide 41: PCB-Level Overview
DRP
VR1
VR2
DBB, APC…
VCore
Locosto
Triton

## Slide 42: DRP-Triton Interface
LoCosto
Triton
0.9V Internal,
Trimmed
To DCXO
To DRP
VR2=2.78V
1.4V , 5mA 1 F external cap Low Noise at low frequencies
< 10mA
470 nF
VREXTH
LDOX
BGAP
10 F
1.1V to 1.8V, 30mA 4.7 F external cap Low Noise at high frequencies
LDOA
To RF
To ABB
To DCO
1.1V to 1.8V , 30mA 1 F external cap Low Cost-Area
1.1V to1.8V , 30mA 1 F external cap Low Cost-Area
VR1=2.78V
< 70mA
VRMMC
LDORF
LDOOSC
10 F
IREF
45 k
To DRP
1 F
4.7 F
1 F
1 F
VREXTL
To DRP
VREF
VREF
VREF1

## Slide 43: VREF
VREF pin has high impedance in nature
  Watch for nearby PWB routings
Star connection from VREF
VREF has priority on PWB
  VREF1 is secondary
VREF pad, ball
VBUF
BGAP Core
40 k
360 k
32.5 pF
470 nF
VREF1
0.9V Internal,
Trimmed

## Slide 44: IREF
IREF pin has high impedance in nature
  Watch for nearby PWB routings
AMP
45 k
current mirror
VREF1
IREF pad, ball

## Slide 45: LDOs / VREF / IREF specifications
 | Unit | LDOX | LDOOSC | LDORF | LDOA | VREF
Vout typ (after trim) | V | 1.4 | 1.4 | 1.4 | 1.4 | 0.9
Max average current (during 625us) | mA | 5 | 30 | 30 | 30 | -
External Cap | uF | 1 | 4.7 | 1 | 1 | 0.47
Main "function" |  | Low noise @low freq | Low noise @high freq | Low cost-area | Low cost-area | 
Vout range | V | 1.393/1.407 | 1.2/1.8 | 1.1/1.8 | 1.1/1.8 | 0.882/0.918
Tied to |  | DCXO Temp sensor buffer | DCO Freq divider Buffers | PPA SAM LNTA | ABB | 
Noise typ (1kHz) | nV/Hz^0.5 | 0.25 | 6.3 | 6.3 | 6.3 | 
Noise typ (400kHz) | nV/Hz^0.5 | 27 | 9.1 | 23 | 23 | 16

## Slide 46: LDO Key Specifications/Care-about
Cost
  -External capacitor size
  -Silicon area
Nominal voltage
- 1.4 V after trim
Iload,max,avg
- 30 mA except LDOX of 5 mA
Active and passive disable
PSRR relaxed (Since VR1 and VR2 are regulated)
  - Reduced LDO bandwidth
  - Better noise performance
Turn-on time
- (1% settling) < 150 s
- Measured: < 80 s for all LDOs in MS4 data

## Slide 47: LDO Noise Measurements
Currently LDOs provide satisfactory noise performance according to transceiver parametric data
  All LDOs have similar noise performance
  LDOOSC, LDORF and LDOA have better low-frequency noise than spec.
  Plan to unify LDO design for future generations
  Plan to further reduce power/ground domains for future generations, which also further reduces cost

## Slide 48: Power Management
DRP2 needs 3 external power supplies:
VCORE: DRP Core digital supply: 1.3 V
  VCORE is connected to DBB core voltage VDD_CORE.
  Total consumption on this power domain (DRP + DBB) is 140 mA (DRP ~35mA).
  This power domain must be present before all other DRP mega module supplies.
  Low voltage mode: to reduce leakage during sleep mode (voltage reduced to 1.05V)
VR1: Pre-regulated input to LDO_OSC,LDO_A and LDO_RF DRP embedded LDOs. The required supply is 60 mA at 2.8V.
  This power domain is isolated from the VCORE allowing VR1 switch off while keeping VCORE active or in low consumption mode.
VR2: Pre-regulated input to LDO_X DRP embedded LDO.
  The required supply is 10 mA at 2.8V. This power domain is isolated from the VCORE allowing VR2 switch off while keeping VCORE active or in low consumption mode

## Slide 49: Power Management sequencing
VCORE is provided first at start-up
Then VR2 (DCXO) is provided by Triton, then VR1 for other RF blocks.
VCORE and VR2 sequencing is controlled by Triton FSM.
VR1 is switch ON/OFF is controlled by SW.

## Slide 50
Digital RF Processor
APC

## Slide 51: APC in Wrapper - Triton Interface
Triton
VR2=2.8V
< 10mA
VREXTH
10 F
VR1=2.8V
< 70mA
VRMMC
10 F
VREXTL
VCORE=1.3V
LOCOSTO
WRAPPER
LDOA
LDOOSC
LDOX
LDORF
BG
VREF
IREF
DRP
Band-Gap
LDO
APC
Ctrl
APC
DAC
APC
OUT
100nF APC_VREF 0.9V
100nF APC_LDO_FILTER 1.4V
APC VDO

## Slide 52: APC Power Management
APC power supply requirements –
VCORE: Core digital supply (1.3 V). This supply is dedicated to the APCD (APC Digital) block.
VRAPC: Pre regulated supply to APC DAC analog output stage. The required supply is 20 mA at 1.4V.
  This power domain is provided through an integrated LDO, SW controlled through the DBB.
VDD_APC: APC Output Amplifier power supply. The required supply is 6 mA at 2.8V, this to allow an adequate APCOUT signal swing capable of driving PA circuits.
  This domain is mapped on the Triton VRMMC supply with star connection respect to the DRP VR1 input to reduce noise. This power domain is enabled under SW control.

## Slide 53: DRP - APC
Locosto
APC is integrated in the DRP Wrapper
DRP
Wrapper
DBB
Triton
APC

## Slide 54: DRP - APC
APCD : Digital block generating the correct ramping profiles
APCDAC : Digital to Analog Converter and output stage of the APC.

## Slide 55
In previous TI modem applications,
-TX ramping up and ramping down were achieved during 8 GSM bit.
-One ramp shape was described using 1 coefficient every ½ bit  16 coefficients
-Output data rate was every 1/8 GSM bit by interpolating linearly by a factor 4.
Now in Locosto application,
-TX ramping up and ramping down are achieved during 5 GSM bit.
-One ramp shape is described using 1 coefficient every 1/4 bit  20 coefficients
-Output data rate is every 1/4 GSM bit (4*270.833kHz). No more interpolation.
Remains unchanged:
-Coefficients are still 8-bit coded.
-Coefficients are stored in a dedicated RAM
-Last power level is stored for smooth transition in multi-burst mode
-Ramping profile is given by the following equation :
DRP - APC :Ramp Generation

## Slide 56
DXP-APC: Ramp Generation
Levelinit
Up[1]
Up[20]
Up[i]
0<=Up[i]<=255
Levelfinal
steplevel
Signstep=0 or 1
In this case,
as it is a ramp-up,
Signstep=0
Level(i)
5 GSM bit = 20 GSM qbit

## Slide 57
Ramp timings and triggering
  Simple interface for enabling/triggering APC ramp up/down
    APC_LDO_EN : controls APC LDO ON/OFF
    APC_EN : enables APC core
    APC_START : Begins ramp sequencing
  2 modes
    Internal sequencing : ramps are automatically generated each timeslot (default used in Locosto)
    External trigger : TSP is responsible for triggering ramp up/down each burst
  Programmable delays between trigger and start of ramp up/down
    APC_DEL_DWN : delay between trigger and start of ramp up
    APC_DEL_UP : delay between trigger and ramp down
DRP - APC

## Slide 58
Internal sequencing (default mode)
External trigger
DRP - APC

## Slide 59
Digital RF Processor
Receiver
Gain strategy

## Slide 60: Receiver Gain-Settings
Sub-block gains : LNA, TA/Mixer, CTA
Filter corners : TA/Mixer, SCF

## Slide 61: Receiver Gain-Settings (cont.)
The DRP will split the global gain across the receive chain according to internal strategy (calibration/compensation).
2 levels should be pre-defined for AFE gain (only 1 bit kept in case more steps needed)
  Low Gain (11 dB)
  High Gain (38 dB) : 24 dB LNA / 10 dB TA / 4.4 SCF
(9) levels should be defined for ABE gain: 0, 2, 5, 8, 11, 14, 17, 20, 23 dB
2 bandwidths settings should be available for switched cap filter SCF (270 kHz, 170 kHz)

## Slide 62
Digital RF Processor
Clock management

## Slide 63: Clock manegement

## Slide 64
Clock Management Overview
Triton
Locosto
DRP
DPLL
APLL
CLKM
32KHz
CLK13EN
DBB
NR - Non Retimed/Regenerated
R - Retimed/Regenerated
ULPD
Wakeup Req
Periph.
13MHz(NR)
13MHz(NR or R)
104MHz(NR)
104MHz(NR)
104MHz(NR or R)
48MHz

## Slide 65: System Clock
In order to reduce the digital switching noise, it is desirable to have all DBB clocking signals synchronous to the DRP’s local oscillator (LO) clock.
The DRP’s CKM function includes a re-synchronization mechanism offering the capability for locking reference clock on the LO clock edges.
The DRP outputs to versions of the 13MHz clock:
  DRP_DBB_DPLL_CLK which is a divided by two version of FREF (26MHz). This clock is a non retimed 13MHz clock and is only used by the DPLL (DPLL needs a non retimed version of the system clock due to the cycle accuracy required by the gauging algorithm).
  DRP_DBB_SYS_CLK is the 13MHz system clock sent by the DRP to the DBB clock manager. This clock can be retimed or non-retimed.
    Default mode: clock is retimed when ADPLL is in tracking mode (switch from non-retimed to retimed clock is managed automatically by the DRP)
    Disable mode: by SW, retiming can be completely disabled.

## Slide 66: System Clock Retiming
Retiming consists in passing the non retimed clock into flops operating at CKV (RF clock), CKV/2 or CKV/8 frequency. Clocks are not re-generated (stable clock frequency) but just re-synchronized with a CKV derived clock. The muxing between retimed and non-retimed modes of operation does not lose any pulses.

## Slide 67: DSP/MCU Clock Regeneration
To reduce the digital switching noise, MCU/DSP 104MHz clock also needs to be synchronous to the RF clock (ADPLL clock).
DPLL block uses the DRP non-retimed 13MHz clock to generate the 104MHz. This 104MHz from DPLL is only used by ULPD (for gauging).
MCU/DSP don’t directly use this clock but use a regenerated version of this clock.
DPLL clock is sent to DRP for regeneration. DRP muxes this clock with a generated version of this clock to provide the DSP/MCU clock.
When RF is in idle state, the clock output by DRP is the DPLL clock.
When in Tx or Rx and once the ADPLL has settled (when in tracking mode), DRP creates the DSP clock by dividing the ADPLL clock by integer value.
As a consequence, while in Tx or Rx, the MCU & DSP clock can vary from 104.1 MHz to 110.4 MHz depending on the Rx/Tx RF channel.

## Slide 68: DSP/MCU Clock Regeneration

## Slide 69: DSP/MCU Clock Regeneration
Switch between DPLL clock and regenerated clock is completely handled by DRP, no action is required from DBB (DBB can only choose by SW programming to completely disable the retiming).
Division factors inside DRP are chosen so that minimum MCU/DSP frequency is 104MHz. So when regeneration is activated (when ADPLL is in tracking mode), DSP and MCU will see their respective clocks increased.
ADPLL frequency varying from 1648MHz to 1990MHz depending on the RF channel, a division factor going from 15 to 19 is applied to the RF clock in order to guaranty a minimum DSP/MCU clock frequency of 104MHz.
Hence DBB frequency can then vary from 104.1 MHz to 110.4 MHz depending on the RX/TX RF channel.

## Slide 70: DSP/MCU Clock Regeneration

## Slide 71
Digital RF Processor
Script Processor
and SRM

## Slide 72: Script Processor & SRM

## Slide 73: Control-Centric Diagram of DRP2
Module | Functions
SCR2 – Second Generation Script Processor | Processor used for DRP control and compensation
SRM – Shared RAM Module | RX and TX data buffers; script buffer; analog control word regs.
OCP – OCP Module | OCP address decode and master/slave connections
DTST – Digital Test Module | JTAG access and digital test mux
DCXOIF – DCXO Interface Module | DCXO interface; power-up state machine
CKM – Clock Module | Clock gating and muxing; clock division and control
ARXCW – ABE control | Registers that control ABE configuration
Locosto DRP2 Wrapper | Interface to Calypso DBB; Extra RAM for script storage

## Slide 74: Script Processor
The Script Processor is a DRP2 module whose main purposes are:
  Provide simple API to the digital baseband
  Perform calibration and compensation of the analog and RF front-end
SCR2 can perform operations based on a preloaded “scripts”
SCR2 has the following hardware resources:
  Registers (scalar, vector)
  32 bit ALU, Multiplier, a sequential divider
  Boolean logic
  OCP master and slave interfaces
  Wall-clock timer
  Wait on hardware event
The SCR2 has no internal RAM, so it uses a section of the SRM memory to store program instructions (scripts) and data. It can also use external RAM (in Locosto wrapper) for storage. There is no performance difference between using SRM RAM or external RAM as Locosto wrapper supports zero wait state response.

## Slide 75: SCR2 Script Control
The SCRIPT_PTR_0 to SCRIPT_PTR_15 registers are used for storing the start addresses of the scripts.
The SCRIPT_START register has to be programmed with script numbers that need to be executed on a particular triggering condition.
There are two ways of starting a script:
  Event-triggered. Currently edges of TX-START and RX-START signals are considered for script triggering.
  Set the script_start bit in the SCRIPT_START register. Writing ‘0’ to this bit stops any running script.

## Slide 76: Shared RAM Module
The Shared RAM Module (SRM) provides the following functions:
  Single time-shared data storage RAM used for TX data, RX data and scripts
  Memory-mapped access to the control words for analog modules
  RX data buffer and interface to the DRX module
  TX data buffer and interface to the DTX module
  Script processor instruction buffer
  CALC data buffer for SCR
  Read access to DRP2 EFUSE data (where bandgap trimming values are stored)
RAM size is 1024 * 32 bits words (4kbytes) and mapped into the OCP memory space

## Slide 77: SCR2 Wrapper Memory
4 kBytes RAM added into the wrapper to extend SCR memory:
  Needed to store the scripts, compensation algorithms and calibration tables
  This memory can be accessed via OCP bus (OCM port) => it is accessible by the 3 processors (SCR / MCU / DSP)
DRP2
OCP1
OCP2
OCPM
TPU2OCP
TPU
DSW_OCPRHEA
OCP2MEM
MEMORY
1k X 32 bit
DSP
RHEA Bus
ARM RHEA Bus
APC
RHEA SWITCH
Programmable Mask
drp_dbb_rx_it
DMA, IT handler

## Slide 78
Digital RF Processor
DRP Wrapper

## Slide 79: DRP Wrapper

## Slide 80: DRP Wrapper
    Bus I/F (RHEA/OCP bridges)
      DSP-DRP Control & data path
      MCU/DMA-DRP Control & data path
    TPU2OCP I/F
      Q-bit timed event control from DBB to DRP
      Q-bit timed event from DBB to Front End Module & Power Amplifier (TSPACT’s)
    Power, reset & Clock system management
      Power-up sequencing
      Programmable startup timer (RHEA bus)
      DCXO & Retimed Clock control
    Interrupt & DMA Request
      Rx events Programmable mask counter (RHEA bus)
    Calibration/Compensation RAM
      4-KByte RAM Shared DBB/DRP
      XIP for DRP’s Script-Processor
      DSP & MCU/DMA access for calibration scenario load/pre-set
    APC function
    TEST & debug DBB/DRP alignment (TAP/JTAG, eFuse…)

## Slide 81: DRP Wrapper Overview
CLKM
DRP
DPLL
INTH
TPU
MCU/DMA RHEA BUS
DSP RHEA BUS
ULPD
DMA
Handler
DBB
TPU2OCP
Bus interface
Clock and Power management
INT &
DMA REQ
DRP
Wrapper
TEST BLOCK
OCP1
OCP2
INT
DCXO & CLOCK
TEST
JTAG
FUSE
SCAN
TEST
APC
OCPM
Memory

## Slide 82: Bus Interface
TPU2OCP
RHEA_SWITCH
OCP2MEM
MEM
32X1k
APC
DRP wrapper
OCPS#1
DRP2
DSW_OCPRHEA
OCPS#2
OCPM
DCXO_MGMT
ULPD
TPU
MCU/DMA
rhea
DSP rhea
DRP2 has three OCP busses: two slaves and one master managed by the internal script processor.
OCP1 and OCP2 slave busses are two identical 16 bits data interfaces dedicated to access internal registers.
OCP1 bus has the priority on OCP2 bus.
OCP master bus is used by the script processor to access scripts located in wrapper memory.
All the memory space (8 Kbytes) allocated to the DRP2 is accessed through OCP1 & 2.

## Slide 83
MCU (DMA) and DSP are both connected on OCP2 bus and they have their own Rhea bus.
The arbitration and conversion from Rhea to OCP is done by the DSW_OCPRHEA module.
TPU2OCP
RHEA_SWITCH
OCP2MEM
MEM
32X1k
APC
DRP wrapper
OCPS#1
DRP2
DSW_OCPRHEA
OCPS#2
OCPM
DCXO_MGMT
ULPD
TPU
MCU/DMA
rhea
DSP rhea
DSW_OCPRHEA

## Slide 84: TPU2OCP
As TPU access are more constrained, it is connected on OCP1 (OCP1 higher priority than OCP2) bus through the TPU2OCP module.
TPU used a parallel 8 bits data bus to access the TPU2OCP, which executes the OCP access when requested by TPU.
TPU2OCP module is based on the previous TSP interface with an OCP master interface replacing the serial interface.
TPU2OCP
RHEA_SWITCH
OCP2MEM
MEM
32X1k
APC
DRP wrapper
OCPS#1
DRP2
DSW_OCPRHEA
OCPS#2
OCPM
DCXO_MGMT
ULPD
TPU
MCU/DMA
rhea
DSP rhea

## Slide 85: DCXO MANAGEMENT
DCXO_MGMT module manages the DCXO clock in the DBB chip.
It manages DRP2 DCXO interface during the following events
  Power-up
  Sleep on
  Wake-up
It requests and cuts the DCXO clock according to the external Triton clock request.
TPU2OCP
RHEA_SWITCH
OCP2MEM
MEM
32X1k
APC
DRP wrapper
OCPS#1
DRP2
DSW_OCPRHEA
OCPS#2
OCPM
DCXO_MGMT
ULPD
TPU
MCU/DMA
rhea
DSP rhea

## Slide 86
DCXO Management in System View

## Slide 87
Digital RF Processor
DRP Timing

## Slide 88: Power On Sequence
26MHz is switched on and Triton LDOs are on
Scripts are loaded by the MCU to the script processor memory (SRM)
Then MCU switches on the RF LDOs by calling the REG_ON script
REG_ON script is triggered by RF_INIT
  VCORE is provided first at start-up
  Then VR2 (DCXO) is provided by Triton, then VR1 for other RF blocks
  VCORE and VR2 sequencing is controlled by Triton FSM
  VR1 is switched ON/OFF by SW

## Slide 89: DRP External Supply Voltage
LoCosto
Triton
0.9V Internal,
Trimmed
To DCXO
To DRP
VR2=2.8V
1.4V , 5mA 1 F external cap Low Noise at low frequencies
470 nF
VREXTH
LDOX
BGAP
10 F
1.1V to 1.8V, 30mA 4.7 F external cap Low Noise at high frequencies
LDOA
To RF
To ABB
To DCO
1.1V to 1.8V , 30mA 1 F external cap Low Cost-Area
1.1V to1.8V , 30mA 1 F external cap Low Cost-Area
VR1=2.8V
VRMMC
LDORF
LDOOSC
10 F
IREF
45 k
To DRP
1 F
4.7 F
1 F
1 F
VREXTL
To DRP
VREF
VREF
VREF1
VCORE=1.3V

## Slide 90: RX Operation – Single Slot

## Slide 91
RX Operation – Multi-Slot

## Slide 92: Masking of The First Rx Interrupts
When RX_Start raises, digital Rx clocks are resynchronized so that 100kHz sine wave has a known initial phase.
Due to the CSF group delay, first Rx I/Q samples are distorted by this re-synchronization and therefore have to be dropped.

## Slide 93: Tx Operation - Single Slot

## Slide 94: TX Operation - Multi-slot

## Slide 95: TX Operation Timeline

## Slide 96: TPU Drivers
TPU is responsible for the real-time control and programming of DRP
Receive operation
  Normal Burst
  Synchronization Burst
  Power Measurement
  Frequency Burst
Transmit operation
  Normal Burst
  Access Burst

## Slide 97: TPU Drivers
rf_init
rf_program
l1dmacro_rx_synth
l1dmacro_tx_up
l1dmacro_tx_down
l1dmacro_rx_down
l1dmacro_rx_up
l1dmacro_init_hw
l1dmacro_rx_nb
l1dmacro_rx_sb
l1dmacro_rx_ms
l1dmacro_rx_fb
l1dmacro_rx_fb26
l1dmacro_tx_nb
l1dmacro_tx_ra
Burst Length
Burst Length
Initialization
RX functions
TX functions
TX
RX
l1dmacro_tx_synth
l1dmacro_agc

## Slide 98: TPU Programming
DRP registers are constituted by:
16 address bits; 16 data bits
1 TPU write to DRP register is done by a 32 bits transfer
  5 TPUMOVE instructions (2 for address, 2 for data, 1 for transfer control)
  OCP transfer
5.15 qbits => Minimum time during two consecutive DRP register programming is 5qbits
OCP registers format
TPU
OCP
Latency
Setting | Value
Address bus | 16 bits
Data Bus | 16 bits
Clock | DSP_CLK / 2 = 52 MHz