## Slide 1
Texas Instruments Shanghai
Wireless Customer Integration & Design Center
* DO NOT COPY *
TI proprietary Information, under Non-Disclosure Agreement
Triton-Lite TWL3031

## Slide 2: Content
Overview
System management.
Power management control
Power-supply
Audio resources.
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping
* DO NOT COPY *

## Slide 3: Content
* DO NOT COPY *
Overview
System management.
Power management control
Power-supply
Audio resources.
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 4: Overview
TWL3031 device provides the following resources :
• System management
• Power Management resources
• Power supply resources
• Voice & Audio resources
• Battery charger & control resources
• Real Time clock resources
• Analog transceivers / drivers resources
• Housekeeping
* DO NOT COPY *

## Slide 5: Overview
TWL3031 Functional Block Diagram

## Slide 6: Overview
* DO NOT COPY *
TWL3031 terminal assignments

## Slide 7: Overview
* DO NOT COPY *
DMA
CDSP subchip
Power
Management
Voice
Codec
Audio
Codec
USB-OTG
transceiver
I2S
I2C
LCD
RAM
NOR
FLASH
NAND
FLASH
BT
AGPS
32 kHz
On/Off
LED
TRITON Lite
ADC aux
Bus Cntl
RTC
LOCOSTO
EMIF
ARM7TDMIE
13 Mhz
ULPD
On_nOff
Wakeup_int
MB
BB
I2C
I2C
LCD
KB
Camera
Companion Chips
NandFlashIf
Cport
Keyboard
VSP
26 MHz
DRP
I2C
Mcsi
UART
32 Khz
SPI
Secondary
LCD
USIM
PA
+
Antenna

## Slide 8: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources.
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 9
System clock
* DO NOT COPY *
System management provides read / write access to configure registers of the embedded resources and manages the interrupt handling.
System clock:
The system clock frequency of TWL3031 is 13-MHz.
MCLK1 System clock input (from host processor)

## Slide 10
* DO NOT COPY *
Control port
One unmarked serial interface provides the mean of communication between TWL3031 and two host
processors (modem and application processor).
After the reset signal, the serial interface has read/write access to all internal registers of TWL3031 device.
SDA1 I2C Bi-directional data signal
SCL1 I2C Bi-directional clock signal

## Slide 11
Interrupt handling
P1_INT2 interrupt signal can be asserted by any TWL3031 resource and sent to the suitable host processor.
Notes: AUC consists of a voice coder-decoder (codec) dedicated to GSM applications and an audio stereo line.
In the uplink path the codec processes analog audio components and transmits this signal to the DSP speech coder through the voice serial port (VSP).
In the downlink path the codec converts the digital samples of speech data received from the DSP via the VSP port into analog audio signals.
the codec supports an 8-kHz (default) or a 16-kHz sampling frequency.
The stereo audio path converts audio component data received from the I2S serial interface (AUSP) into analog audio.

## Slide 12: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources.
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 13
* DO NOT COPY *
Power management control
Power management resources include:
• Power-On Reset, in order to generate a system reset at battery plug-in.
• Power Control State Machine, which controls the power on sequence of the system initiated by external events (Button, Accessory plug / un-plug, …) or internal event (Interrupt, Wake-up event).
Notes: TESRESET : IOTA active low
RPWON: IOTA only edge detection

## Slide 14
* DO NOT COPY *
Power-On Reset
The Power Control State Machine controls the transition sequences among the different operating states of the system
Other function of the Power Control State Machine is to monitor power supply elements and detect power failures or over-temperature conditions.
Notes: Interrupt INT2 is generated either for the following events: PWON, RPWRON, RPWON2, a charger plug/unplug is detected, or an USB plug/unplug is detected while the device is in power on.
Interrupt INT1 is generated when abnormal low battery voltage condition is detected.

## Slide 15
* DO NOT COPY *
System operating state
Five system operating states are defined:
NO SUPPLY: No battery is present.
BACKUP: Only backup battery is present.
OFF: Main battery is present, backup battery present or not.
Default configuration is all power supplies are in off-state except VRTC.
ACTIVE: Main battery is present, backup battery present or not. Power supplies are on.
SLEEP: Main battery is present, backup battery present or not. Power supplies are in low-power mode.

## Slide 16
System operating state
Notes: Power-On Reset (POR): Provides a reset signal for the VRPC state machine, RTC clock and DBB split power logic. This reset signal (nRESPWONZ) becomes high when UPR>2.6V on the rising edge, and low when UPR<2.1V in the falling edge.
SWON: This is a comparison block for the battery voltage and reference (3.2V). The result of this comparison determines whether the switch-on process can be achieved.
BBS (BB Switch), UVLO: This is also a battery voltage comparison block with a reference (2.8V). It determines whether a emergency switch-off event needs to occur. When the voltage drops below 2.8V, an emergency interrupt is generated (INT1) and VRPC automatically executes a switch-off sequence to the BACKUP state.
VRPCD: A digital block that contains the state machine and timers to control the switch-on, switch-off sequences.

## Slide 17
System operating state

## Slide 18
* DO NOT COPY *
System operating state
Reference voltage and reference current:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources.
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 20
* DO NOT COPY *
Power-supply
Three modes are defined for the power supply modules:
OFF: No voltage, no current.
ON: Nominal voltage, nominal output rating current.
LOW POWER: Nominal voltage, low output rating current.

## Slide 21
* DO NOT COPY *
Power-supply
Modem DBB:
Peripherals:
Notes: <number>
<footer>
<header>
<date/time>
During the Watchdog interval, the SW has 150us corresponding to 1950 X 13MHz clock cycles to treat the INT interrupt and execute possible configuration access to enter BACKUP state.

## Slide 22
* DO NOT COPY *
Power-supply
TWL3031:
Notes: <number>
<footer>
<header>
<date/time>
De-bounce period of 1034 * T32K = 32ms.

## Slide 23
* DO NOT COPY *
Power-supply
Power supplies diagram

## Slide 24: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 25
* DO NOT COPY *
Audio resources
TWL3031 provides voice and audio resources:
• Telephone voice codec
• Audio stereo path.
• Clock frequency: same as master clock frequency.
• One SPI (VSP) interface for voice and one I2S serial interface (master) for audio.

## Slide 26
* DO NOT COPY *
Audio resources
Voice Codec characteristics:
8-kHz & 16-kHz sample rate.
13-bit ADC / 15-bit DAC and digital filtering.
Uplink & Downlink PGA, Side tone and volume control.
Microphone and headset microphone bias generation.
Send / End detection (Hook detect1).
Voice memo function through transmission path.

## Slide 27
Voice Uplink
Audio resources

## Slide 28
Voice Downlink
Audio resources

## Slide 29
* DO NOT COPY *
Audio resources
Audio Stereo path characteristics:
Digital interface Sampling rate
8-kHz, 11.025-kHz, 12-kHz, 16-kHz, 22.05-kHz, 24-kHz, 32-kHz, 44.1-kHz, 48-kHz.
15-bits linear stereo DAC, digital filtering.
Independent right and left volume control.

## Slide 30
Audio Stereo
Audio resources

## Slide 31
Audio resources
Audio analog inputs:
Differential microphone input (20-Hz to 8-kHz bandwidth).
Single ended headset microphone input (20-Hz to 8-kHz bandwidth).
Left & Right analog inputs with volume control for FM radio (20-Hz to 8-kHz bandwidth): FM stereo
(through FML and AUXI_FMR pins) and FM mono (through AUXI_FMR pin).

## Slide 32: Audio resources
* DO NOT COPY *
Audio analog outputs:
Microphone and headset microphone bias outputs.
Differential Earphone output.
Single ended headset output.
8-Ohm Hands Free output.
Left & Right Auxiliary outputs.
Left & Right single ended headset outputs.
Pseudo-ground output to avoid AC coupling.

## Slide 33: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources
Battery charger & control
Transceiver & drivers.
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 34
* DO NOT COPY *
Battery charger & control
High voltage (20V) Main battery charger interface:
Allows use of low cost 20V unregulated charger
Capability of charging from USB (Li-Ion, Li-polymer)
Li-Ion, Li-polymer and Ni-Mh battery
Linear charge through constant current / constant voltage modes
Pulsed charge through PWM signal
AC and car-kit pre-charge. Automatic starts and stop depending on main battery voltage
Battery monitoring (Voltage, Temperature, Type, Charge current) done via the general purpose 10bit ADC

## Slide 35
* DO NOT COPY *
Battery charger & control
Notes: <number>
<footer>
<header>
<date/time>
FS = [8~48kHz]
PLL lock time = 10ms

## Slide 36: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources
Battery charger & control
Transceiver & drivers
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 37
* DO NOT COPY *
Transceiver & drivers
TWL3031 provides the following transceivers and drivers:
• SIM-card interface (insertion / extraction detection function);
• USB 2.0 FS transceiver (slave only);
• Vibrator driver;
• White-LED’s drivers.

## Slide 38
* DO NOT COPY *
Transceiver & drivers
SIM-Card interface:
Purpose of the SIM-card interface is to allow use of 1.8V/2.85V SIM-card types.
TWL3031 provides only the insertion / extraction detection function.
All the other signals from / to the SIM-card module (SIO, SCK, SRST) are managed directly by the digital IC companion.

## Slide 39
* DO NOT COPY *
Transceiver & drivers
USB Transceiver:
OTG transceiver specification (compliancy only)
TWL3031 includes a single USB 2.0 Full-Speed (FS) transceiver compatible with the “Universal Serial Bus Specification Revision 2.0”
Mini-USB Analog Car Kit Interface
For compliance with CEA-936-A standard, TWL3031 USB interface supports the following functionalities:
USB digital data.
4 Wire Analog Car-kit.
• UART (RS232) digital data.
• Charge phone.
Notes: The BUL path performs modulation of burst data sent from the DSP radio interface (RIF) to the baseband serial port (BSP).
The modulator circuit in the BUL path performs the Gaussian minimum shift keying (GMSK) in accordance with the 3GPP specification TS 05.04.
The GMSK modulator generates the in-phase (I) and quadrature (Q) components.
These digital I and Q words are converted into analog baseband by two 10-bit DACs and filtered by third-order low-pass filters.
The BUL path includes secondary functions such as dc offset calibration and I/Q gain unbalance

## Slide 40
* DO NOT COPY *
Transceiver & drivers
USB transceiver diagram
Notes: The BDL path converts the baseband analog I and Q components from the RF receiver into digital samples. The resulting signals are filtered through a digital FIR to isolate the desired data from the adjacent channels. During reception of the burst I and Q components, the digital data are sent to the DSP via the BSP at a rate of 270.833 kHz.
The BDL path includes a dc offset calibration.

## Slide 41
* DO NOT COPY *
Transceiver & drivers
Vibrator driver:
TWL3031 includes a vibrator driver. The main features of the vibrator driver are:
• programmable output voltage (a) linear or (b) pulse density modulation (from 1.2V up to 2.7V, 75mA maximum output current) with soft turn-on/turn-off and,
• very low frequency (4-Hz) and variable duty cycle (25 / 50 / 75 / 100%).
Vibrator driver block scheme

## Slide 42
Transceiver & drivers
White-LED’s drivers:
TWL3031 includes three white-LED’s drivers for
the main screen,
the keypad and
the auxiliary screen

## Slide 43
* DO NOT COPY *
Transceiver & drivers
W-LED’s driver block scheme

## Slide 44: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources
Battery charger & control
Transceiver & drivers
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 45
* DO NOT COPY *
RTC
The RTC block is an embedded Real Time Clock (RTC) module, directly accessible from the control port interface, which consists of (1) a 32-kHz oscillator (two-pins architecture) and (2) a RTC module.
The principal features/characteristics of the RTC block are:
• Time information
• Calendar Information
• Interrupt generation
• Time correction

## Slide 46: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources
Battery charger & control
Transceiver & drivers
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 47
* DO NOT COPY *
Hot-Die function
TWL3031 contains a programmable temperature monitoring system (Hot-Die function), which is capable to generate an interrupt when a critical junction temperature is reached within the device itself.
This interrupt (#14) is a request to the software to close non-critical applications to reduce the amount of power drawn from TWL3031, thus reducing the internal dissipation.
The temperature monitoring system is also capable to generate a thermal shutdown signal whenever the temperature further increases. This signal generates an immediate, unconditional reset to the TWL3031 device.

## Slide 48: Content
* DO NOT COPY *
Overview
System management
Power management control
Power-supply
Audio resources
Battery charger & control
Transceiver & drivers
RTC (Real Time Clock)
Hot-Die function and Thermal Shutdown
Housekeeping

## Slide 49
Housekeeping
A general purpose 10-bit ADC provides the means to monitor internal or external parameters. It includes a 11 channel multiplexed inputs arranged as follows:
Internal monitoring (6 channels) for:
• Main Battery voltage
• Main Battery charging current
• Backup battery voltage
• Charger voltage
• USB VBUS voltage
• Internal IC temperature
External monitoring (3 channels):
• One simple input (ADCIN3)
• Two inputs with current sources (ADCIN4 and ADCIN5) for battery type and battery temperature respectively

## Slide 50
Thank you!
* DO NOT COPY *