## Slide 1: Company Presentation
SAP.doc
To
TISD.h and TISD.intf
“Nature just loves to improve on itself”
Heraclitus

## Slide 2: Protocol Stack Development Methods
3GPP
SPECS
Message
Sequence
Charts &
System Design
Requirement
Spec &
Analysis
Single Source
Affected part of
the tool chain
TISD
Compiler

## Slide 3: The SAP compiler chain
The SAP compiler chain contains 3 executables
antiword (or doc2txt)
  Equivalent to save as text
xGen
  Converts the text file to an structured text format (MDF/PDF)
Ccdgen
  Generate h-files for Condat entities
  and tabels for CCD-lib, Trace and Test tools.
  Optional generate SDL include files
  Generate TISD h-files
NEW
NEW
Note: PDF is not to the Adobe acrobat format

## Slide 4: Primitive
#ifndef L1_L1EH_ACTIVATE_REQ_CLASS
#define L1_L1EH_ACTIVATE_REQ_CLASS
/*
*
*/
typedef struct
{
Pub_X_StartModulo startModulo; /*< 0: 1> Pub_X_StartModulo Start point of reception of transport blocks from the PCCPCH (SFN mod start_modulo = 0) */
Uint8 thresholdIncluded; /*< 1: 1> valid-flag */
Pub_X_Threshold threshold; /*< 2: 3> A set of threshold parameters. */
Uint8 singleUarfcnIncluded; /*< 5: 1> valid-flag */
Uint16 singleUarfcn; /*< 6: 2> UMTS Absolute Radio Frequency Channel Number */
Uint8 highPriorityListIncluded; /*< 8: 1> valid-flag */
Uint8 highPriorityListCount; /*< 9: 1> counter */
Pub_X_HighPriorityList highPriorityList[PUB_STD_SIZE_HIGH_PRIORITY_LIST]; /*< 10: 64> List of channel and code combinations to scan with high priority. */
} L1_L1Eh_ActivateReq;
#define L1_L1EH_ACTIVATE_REQ_SIZE(_count) \
( \
sizeof(L1_L1Eh_ActivateReq) \
)
#endif
Fixed size primitives are in the same format except for comments.

## Slide 5: Primitive
#ifndef L1_L1EH_CHANNEL_RELEASE_REQ_CLASS
#define L1_L1EH_CHANNEL_RELEASE_REQ_CLASS
/*
*
*/
typedef struct
{
Pub_X_ActivationTime activationTime; /*< 0: 1> Pub_X_ActivationTime This parameter is the CFN, where the configuration must be activated. */
Uint8 trchTypeCount; /*< 1: 1> counter */
Pub_X_TrchType trchType[PUB_STD_SIZE_TRCH_CONFIG]; /*< 2: 32> Pub_X_TrchType The transport channel type. */
} L1_L1Eh_ChannelReleaseReq;
#define L1_L1EH_CHANNEL_RELEASE_REQ_SIZE(trchTypeCount) \
( \
offsetof(L1_L1Eh_ChannelReleaseReq,trchType) + \
( sizeof(*((L1_L1Eh_ChannelReleaseReq)0)->trchType) * (sCount) )\
)
#endif /* L1_L1EH_CHANNEL_RELEASE_REQ_CLASS */
Variable size primitives are in the same format except for comments.
But a different algorithm is use in the …_SIZE macro

## Slide 6: Interface
Interface =
{
structHdrFile = "L1_L1Eh.h";
inputs =
{
CPHY_ACTIVATE_REQ =
{
primNum = 0x80000080;
primStruct = L1_L1Eh_ActivateReq;
comment = "";
};
…
};
outputs = {
CPHY_ACTIVATE_CNF =
{
primNum = 0x80014080;
primStruct = L1_L1Eh_ActivateCnf;
comment = "";
};
…
};
};
A new file called ”L1_L1Eh.intf” have been created
This file should be included in the .conf file by use of an
C-preprocessor

## Slide 7: Struct
#ifndef PUB_X_ACCESS_SERVICE_CLASS_INFO_CLASS
#define PUB_X_ACCESS_SERVICE_CLASS_INFO_CLASS
/*
* The access service class.
*/
typedef struct
{
Uint8 availSignaturesCount; /*< 0: 1> counter */
Pub_X_AvailSignatures availSignatures[PUB_STD_SIZE_SIGNATURES]; /*< 1: 16> Pub_X_AvailSignatures Available signatures */
Uint8 availSubChCount; /*< 17: 1> counter */
Pub_X_AvailSubCh availSubCh[PUB_STD_SIZE_SUB_CHANNELS]; /*< 18: 12> Pub_X_AvailSubCh Available sub channels */
} Pub_X_AccessServiceClassInfo;
#endif /* PUB_X_ACCESS_SERVICE_CLASS_INFO_CLASS */
Structs are in the same format except for comments.
But the group need to be specified correctly in the SAP document

## Slide 8: enum
/*
* enum to Variable dl_fdd_measurements
* FDD measurements
*/
#ifndef PUB_X_DL_FDD_MEASUREMENTS_CLASS
#define PUB_X_DL_FDD_MEASUREMENTS_CLASS
enum
{
PUB_X_DL_COMP_MODE_NOT_NEEDED_FOR_FDD = 0x0, /* This parameter states if PHY needs downlink compressed mode to be able to do inter-frequency measurements in FDD mode. 0 means that DL compressed mode is not needed. */
PUB_X_DL_COMP_MODE_NEEDED_FOR_FDD = 0x1 /* 1 means that DL compressed mode is needed. */
};
typedef Uint8 Pub_X_DlFddMeasurements;
#endif /* PUB_X_DL_FDD_MEASUREMENTS_CLASS */
Enums are in the same format except for comments.
But the group need to be specified correctly in the SAP document

## Slide 9: Summary
Outstandings
  Compile tools on UNIX host (no host in DK)
  Update SAPS with correct group info (need TISD input)
  Accept of changed …_SIZE implementation (type of variable arrays changed)
  Verification on UNIX host (no host in DK)
Q & A
  We are here the next 2 days
  mailto:jho@condat.dk

## Slide 10
INSIDE