## Slide 1
Frame Body Concept

## Slide 2: Frame Body Concept
Overview
Frame Functionality & Interfaces
Test Interface
System Setup
Layer 1 Interface

## Slide 3: Frame Body Concept
Overview
Frame Functionality & Interfaces
Test Interface
System Setup
Layer 1 Interface

## Slide 4: Frame Body Concept - Overview
Software Architecture
RTOS (Nucleus)
Riviera Frame
FFS
KPD
R2D
RVT
...
GPF Frame
RR
MM
CC
TST
...
L1
Applications
Protocol Stack

## Slide 5: Frame Body Concept - Overview
Software Architecture
RTOS
Nucleus, WIN32, pSOS, VxWorks
Protocol Stack Entities
pei_
Frame vsi_
Virtual OS
OS Extensions:
Passive Model
Routing
Trace
Memory Supervision
Timer Configuration
Startup
Callback
OS Layer os_
Adaptation to RTOS
Callback
Driver
Hardware Abstraction
Callback
_init
Virtual System Interface (VSI)
Protocol Stack Entity Interface (PEI)
Operating System Interface (OS)

## Slide 6: Frame Body Concept - Overview
RTOS (Nucleus)
Frame
OS - Layer
Target
TST
RR
VCMS
RTOS (Windows)
Frame
OS - Layer
Tools
TST
xPanel
TAP
PCO
The same frame is used for target and tools !
Frame in Target and Tools
RVT
MUX

## Slide 7: Frame Body Concept - Overview
Protocol Stack Entities
Entities implement the protocol functionality
State machine
Logic of the GSM/GPRS/UMTS specification (e.g. GSM 04.08)
No direct access to RTOS resources
Main loop of process (active body)

## Slide 8: Frame Body Concept - Overview
Frame Functionality
Task Management
Memory Management
Communication
Timer Management
Routing
Tracing
Test Interface
RTOS Access
Main loops of processes (passive body)

## Slide 9: Frame Body Concept - Overview
OS Layer Functionality
Adaptation to the RTOS
RTOS dependent diagnose
Platform dependencies – Nucleus MNT & ARM7
OS interface is independent of RTOS

## Slide 10: Frame Body Concept - Overview
Tasks
Memory
  Dynamic Memory
  Partition Memory
Timer
Semaphores
Interrupt handling (HISR)
Real-time Operating System (Nucleus)

## Slide 11: Frame Body Concept - Overview
Interfaces
Body
OS Layer
RTOS
PEI
OS
Frame
VSI
pei_create()
pei_init()
pei_exit()
pei_primitive()
pei_signal()
pei_timeout()
pei_config()
pei_run()
os_...Task
os_...Queue
os_...Timer
os_...Semaphore
os_...Memory
(os_...Drv)
vsi_c_... - Communication
vsi_t_... - Timer
vsi_s_... - Semaphore
vsi_m_... - Memory
vsi_d_... - Driver
vsi_o_... - Output/Trace

## Slide 12: Frame Body Concept
Overview
Frame Functionality & Interfaces
Test Interface
System Setup
Layer 1 Interface

## Slide 13: Frame Body Concept – Entity Interface
Protocol Stack Entity Interface (PEI)
pei_create() - export entity creation parameters
pei_init() - open communication channels, initialize entity
pei_exit() - close communication channels, free resources
pei_primitive() - process primitives
pei_timeout() - process timeouts
pei_signal() - process signals
pei_config() - dynamic entity configuration
pei_run() - main loop for active body configuration

## Slide 14: Frame Body Concept – Entity Interface
Parameters exported by pei_create()
static T_PEI_INFO pei_info =
{
CC_NAME,
{ /* pei-table */
pei_init,
pei_exit,
pei_primitive,
pei_timeout,
NULL, /* pei_signal, */
NULL, /* pei_run, */
NULL, /* pei_config, */
pei_monitor
},
CC_STACK_SIZE,
CC_QUEUE_ENTRIES,
CC_PRIORITY,
CC_TIMERS,
CC_PROC_TYPE /* ACTIVE/PASSIVE body */
};

## Slide 15: Frame Body Concept - Startup
System Startup (1) – Root Task Context
Create Tasks
  Call pei_create() functions from task list
  Create tasks with the parameters exported by pei_create()
Nucleus initialization
Call of Application_Initialize()
Call of StartFrame()
Initialize Frame
  Create memory pools
  Initialize global tables
Start Tasks

## Slide 16: Frame Body Concept - Startup
System Startup (2) – Created Task Context
TaskEntry ( TaskHandle ) called by the RTOS
{
  Create input queue
  Entity initialization -> pei_init()
  If ( ACTIVE_BODY)
  pei_run()
  while (1) /* PASSIVE_BODY */
  {
    Wait for message
    Process message
  }
}
The same task entry function for all tasks
Each task has its own stack, stack size and priority

## Slide 17: Frame Body Concept - Startup
Task List
const T_COMPONENT_ADDRESS sim_list[] =
{
{ sim_pei_create, NULL, ASSIGNED_BY_CONDAT },
{ NULL, NULL, 0 }
};
const T_COMPONENT_ADDRESS mmgmm_list[] =
{
{ mm_pei_create, NULL, ASSIGNED_BY_CONDAT },
{ gmm_pei_create, NULL, ASSIGNED_BY_CONDAT },
{ NULL, NULL, (int)"MMGMM" }
};
const T_COMPONENT_ADDRESS rr_list[] =
{
{ rr_pei_create, NULL, ASSIGNED_BY_CONDAT },
{ NULL, NULL, 0 }
};
const T_COMPONENT_ADDRESS *ComponentTables[]=
{
...
sim_list,
mmgmm_list,
rr_list,
... }

## Slide 18: Frame Body Concept - Startup
Active/Passive Body
Active Body Passive Body
Main Loop Location Entity Frame
Main Loop Function pei_run() pf_TaskEntry()
Functionality customer defined waiting for message
processing message
Selection of active or passive is done with flags exported by pei_create()

## Slide 19: Frame Body Concept - Startup
Create New Entity
add pei interface by using the template xxx_pei.c
add address of xxx_pei_create() to task list
add source files for further functionality

## Slide 20: Frame Body Concept - Startup
Task Management
  Protocol Stack
    Protocol stack entities run in their own RTOS task or may be grouped in one task, e.g. CC, SS, SMS, SM are grouped to the CM task.
    Tasks are created at initialization
    Static priorities set during initialization
    Scheduling is done by RTOS (preemptive multitasking)
  Tools
    Frame as shared DLL
    Different applications are dynamically started and stopped

## Slide 21: Frame Body Concept – Memory Management
Partition Memory Management (1)
Fixed sized buffers of different sizes ->xxxconst.h
Dynamic memory : MALLOC(size) -> vsi_m_new(size)
MFREE(ptr) -> vsi_m_free(ptr)
ptr
size
cnt

## Slide 22: Frame Body Concept – Memory Management
Partition Memory Management (2)
Static primitives: PALLOC(name) -> vsi_c_new(size)
PFREE(ptr) -> vsi_c_free(ptr)
ptr
size
Header
Primitive header is initialized by the VSI functions

## Slide 23: Frame Body Concept – Memory Management
Partition Memory Management (3)
ptr
size
Header
guess
Dynamic pimitives:
DRPO_ALLOC(name,guess) -> vsi_drpo_new(size,opc,guess)
ptr1
Header
ptr2
DP_ALLOC(ptr,size) -> vsi_dp_new(ptr,size)
FREE(ptr) -> vsi_free(ptr)

## Slide 24: Frame Body Concept - Communication
1 Input Message Queue for each Entity
Primitives -> low priority
Signals -> high priority
Communication between Entities with primitives
  Sender
    Allocate a memory partition (PALLOC)
    Store primitive data in partition
    Write partition address to destination queue (PSEND)
  Receiver
    Read partition address from input queue
    Process primitive - Call pei_primitive()
    Free partition (PFREE)

## Slide 25: Frame Body Concept - Communication
Example Interprocess Communication
.
.
.
.
.
.
.
.
.
.
.
.
1. Allocate Partition
Addr
Process
3. Send Primitive
2. Store Primitive Data
Partition Pool
4. Receive Primitive
5. Process Primitive
6. Deallocate Partition
Addr
Queue
Addr
Addr
Data
Data

## Slide 26: Frame Body Concept - Communication
Expressions
entity = process
primitive = struct
SAP = number
1 input queue per process
entity = process
entity = process
SAP
SAP
SAP
queue
queue

## Slide 27: Frame Body Concept - Communication
Primitive Processing
Header in each primitive
  operation code (opc) 16/32 bit
    SAP number
    primitive number
    uplink/downlink
    protocol/system primitive
  length
  …

## Slide 28: Frame Body Concept – Timer Management
Timer Management
Start
  Timer start request by an entity
  Frame starts RTOS timer
  ATTENTION: timer index has to be in the range between 0 and the number of timers exported by pei_create()
Expiration
  RTOS calls timeout routine in the frame
  Frame calls pei_timeout() in the body
Configuration
  speed up/slow down/suppress
SHORT vsi_t_start ( T_HANDLE caller, USHORT index, T_TIME time )
SHORT vsi_t_stop ( T_HANDLE caller, USHORT index )
SHORT vsi_t_status ( T_HANDLE caller, USHORT index, T_TIME *time )
SHORT vsi_t_config (T_HANDLE caller, USHORT index, UBYTE mode, ULONG value )

## Slide 29: Frame Body Concept – Semaphore Management
Semaphore Management
open semaphore
  create if not existing
  return handle if existing
  initial count
obtain
release
T_HANDLE vsi_s_open ( T_HANDLE caller, char *name, USHORT count )
SHORT vsi_s_get ( T_HANDLE caller, T_HANDLE handle )
SHORT vsi_s_release ( T_HANDLE caller, T_HANDLE handle )
SHORT vsi_s_status (T_HANDLE caller, T_HANDLE handle, USHORT *count )

## Slide 30: Frame Body Concept - Routing
Routing
Redirection and duplication of primitives
Dynamic configuration via test interface
Filters available to select a subset of primitives
Examples
RR DUPLICATE MM PCO all primitives RR sends to MM are duplicated to PCO
RR REDIRECT ALL TAP all primitives RR sends are redirected to TAP
MM DUPLICATE RR 0000011000000001 PCO duplicate RR_ACTIVATE_REQ to PCO
RR REDIRECT MM NULL all primitives RR sends to MM are discarded
RR REDIRECT CLEAN clean all redirections of RR

## Slide 31: Frame Body Concept - Routing
Routing - Observation
Monitoring of primitive communication
MM
RR
PCO
RR DUPLICATE MM PCO
MM DUPLICATE RR PCO

## Slide 32: Frame Body Concept - Routing
Routing - Test
Test of a single entity in the protocol stack
MM REDIRECT CC TAP
MM REDIRECT RR TAP
RR REDIRECT MM NULL
CC REDIRECT MM NULL
MM
RR
TAP
CC

## Slide 33: Frame Body Concept - Routing
Routing - Manipulation
Manipulation of primitive contents
RR REDIRECT MM TAP
MM REDIRECT RR TAP
MM
RR
TAP

## Slide 34: Frame Body Concept - Routing
Routing - Simulation
Run entities on different platforms (target, PC)
MM REDIRECT RR NULL
MM REDIRECT CC NULL
CC REDIRECT MM XMM
RR REDIRECT MM XMM
MM
RR
XMM(PC)
CC

## Slide 35: Frame Body Concept - Tracing
A Way to Follow the System State without Debugger
MM
RR
TST
CC
PCO
TST
Tools
Target

## Slide 36: Frame Body Concept - Tracing
Trace Functionality
  Trace Classes
    Function Traces TRACE_FUNCTION()
    Primitive Traces PTRACE_IN(), PTRACE_OUT()
    State Traces GET_STATE(), SET_STATE()
    Error Traces TRACE_ERROR()
    Event Traces TRACE_EVENT()
    System Traces within Frame
    CCD Traces within CCD
  Comparison of trace class with trace mask in the frame
  Dynamic activation of traces via system primitives
  Binary coding of strings to be traced
  Customer can define his own trace classes

## Slide 37: Frame Body Concept – System Primitives
Read Resource Information
STATUS TASK
Name: RR Stat: 6 Count: 288 Prio: 205 Stack: 871240 Size: 1736 Untouched: 808
STATUS QUEUE
Name: RR Addr: 879188 Entries: 10 Used: 0 MaxUsed: 4
STATUS PARTITION
Name: POOL10 Addr: 85c998 PoolSize: 7128 PartSize: 64 Free: 86 Used: 13
STATUS MEMORY
Name: CONDAT Addr: 86e634 Size: 60000 Min: 4 Free: 12548 Suspend: 6
STATUS SEMAPHORE
Name: CCD_COD Count: 1 Suspend: 11 Waiting: 0

## Slide 38: Frame Body Concept – Partition Supervision
Partition Pool Monitor - Functionality
Monitoring of the partition states
state
owner
last user (file,line)
time
Statistics on partition usage
Sizes of used partitions
Numbers of used partitions
Dump via test interface

## Slide 39: Frame Body Concept – Partition Supervision
Partition Pool Monitor - Output
Allocated Partitions
[PPM]: PARTITION 0x85ed88, OPC 0x0 STATE ALLOCATED OWNER UART, TIME 670, uart_dtxf.c,245
[PPM]: PARTITION 0x85edd8, OPC 0x0 STATE ALLOCATED OWNER MMI, TIME 666, aci_lst.c,147
Statistics
[PPM]: POOL NAME: PRIM
[PPM]: POOL 0 (size 60)
[PPM]: MAXBYTE pool 0: 1849 bytes => 61 %
[PPM]: MAXBYTE partitions pool 0: 5, 0, 3, 41, 1
[PPM]: MAXPART pool 0: 50 partitions => 50 %
[PPM]: MAXPART partitions pool 0: 5, 0, 3, 41, 1
[PPM]: MAXRANGE partitions pool 0: 6, 3, 11, 41, 4
[PPM]: TOTAL partitions pool 0: 17, 23, 541, 497, 115

## Slide 40: Frame Body Concept – Error Handling
Error Handling – System Warnings
SYSTEM WARNING: Waited for space in task queue
SYSTEM WARNING: Waited for partition in task, size size, opc opc
SYSTEM WARNING: Bigger partition allocated than requested, task, size
SYSTEM WARNING: Partition Deallocation failed in task
SYSTEM WARNING: task freed partition stored in task queue
SYSTEM WARNING: Freed partition sent in task, opc
SYSTEM WARNING: Receiver process task unknown
SYSTEM WARNING: Invalid system primitive string
SYSTEM WARNING: Number of written > requested partition size in file, line
System warning results in
Dump of system state
dar_diagnose_write (warning_string, DAR_WARNING, CONDAT_FRM_USE_ID)

## Slide 41: Frame Body Concept – Error Handling
Error Handling - System Errors
SYSTEM ERROR: Number of Timers > MAX_TIMER
SYSTEM ERROR: Number of entities > MAX_ENTITIES
SYSTEM ERROR: Number of started timers > MAX_SIMULTANEOUS_TIMER
SYSTEM ERROR: Number of created semaphores > MAX_SEMAPHORES
SYSTEM ERROR: Partition Guard Pattern destroyed task, ptr, opc
SYSTEM ERROR: No Partition available, task, size
SYSTEM ERROR: task write attempt to dest queue failed
SYSTEM ERROR: task Stack overflow
SYSTEM ERROR: Error at creating task Queue
SYSTEM ERROR: TimerIndex > NumOfTimers for task
System error results in
Dump of system state
dar_generate_emergency (error_string, ..., CONDAT_FRM_USE_ID)

## Slide 42: Frame Body Concept – Error Handling
Error Handling - System State Dump
TST: task state: NU_READY queue state: 0 of 50 used
TST: NU_READY - Normal suspend, Link Register = 0x81186b
TST: Processed Message: SIGNAL opc: 0x8, time: 26149 ptr: 0x85f7bc
MMI: task state: NU_QUEUE_SUSPEND (MMI) queue state: 0 of 20 used
CST: task state: NU_READY queue state: 2 of 10 used
CST: NU_READY - Normal suspend, Link Register = 0x810ded
CST: Messages in queue: TIMEOUT opc: 0x1, time: 0 ptr: 0x0
CST: Messages in queue: PRIMITIVE opc: 0x5600, time: 27916 ptr: 0x863c24
SIM: task state: NU_QUEUE_SUSPEND (SIM) queue state: 0 of 10 used
CM: task state: NU_QUEUE_SUSPEND (CM) queue state: 0 of 10 used
MMGMM: task state: NU_READY queue state: 1 of 10 used
MMGMM: NU_READY - IRQ suspend, Program Counter = 0x1ad54c
MMGMM: Processed Message: PRIMITIVE opc: 0x8000, time: 26149 ptr: 0x85f82c
MMGMM: Messages in queue: PRIMITIVE opc: 0x4608, time: 26690 ptr: 0x85ff2c

## Slide 43: Frame Body Concept
Overview
Frame Functionality & Interfaces
Test Interface
System Setup
Layer 1 Interface

## Slide 44: Frame Body Concept – Test Interface
Running as a Task
Test Interface Functionality
  Input from test system
    System primitives (configuration)
    Protocol primitives
  Output to test system
    Traces
    Routed protocol primitives
Simple exchange of drivers

## Slide 45: Frame Body Concept – Test Interface
Test Interface Driver List
  Name
  Address of drv_Init()
  Process to be notified
  Default configuration
const T_DRV_LIST_ENTRY DrvList[] =
{
{ NULL, NULL, NULL, NULL },
{ "TIF", TIF_Init, "TST", NULL },
{ "TR", TR_Init, NULL, NULL },
{ "SER", SER_Init, NULL, &SER_DefaultConfig },
{ NULL, NULL, NULL, NULL }
};

## Slide 46: Frame Body Concept – Test Interface
Primitive Converter (PCON)
exchange of primitives between platforms with different number representation (little vs. big endian)
exchange of primitives between platforms with different alignment model
exchange of primitives containing pointers
can be called in TIF driver when primitive is sent or received

## Slide 47: Frame Body Concept – Test Interface
Dynamic Entity Configuration
Send strings transparently through TST and the frame to entity
Frame
TST
MMI
xPanel
MMI CONFIG AUTO_ATTACH
pei_config()
AUTO_ATTACH
Used for
Entity configuration GMM CONFIG MULTISLOT_CLASS=<8>
AT commands MMI CONFIG AT+CFUN=1
Timer configuration L2R CONFIG TIMER_SET TUP_SND 1000

## Slide 48: Frame Body Concept – Test Interface
MTST
SER
TI_TRC
UART
RVT
Test Interface – Target Driver Configuration
TST
TIF
TR
FRAME
ACI
serial driver
– SER_fd...
serial driver
– SER_tr...

## Slide 49: Frame Body Concept
Overview
Frame Functionality & Interfaces
Test Interface
System Setup
Layer 1 Interface

## Slide 50: Frame Body Concept – System Setup
Configuration Files
xxxcomp.c
  Task list
xxxdrv.c
  Test interface driver list
xxxinit.c
  Application_Initialize() function
xxxconst.h
  Number and size of partitions
  Number of tasks, timers, semaphores
No frame recompilation when configuration files are changed

## Slide 51: Frame Body Concept – System Setup
Provided Frame Libraries
frame task management, communication, memory, timers, Semaphores,
error handling
tif test interface, drivers
misc common services
Extensions
_na7 nucleus arm7
_npc nucleus MNT (PC Simulation)
_wn WIN32
_db debug
_ps partition pool supervision
_pc pcon
_ir running in internal RAM
_fl running in flash
Examples: frame_na7_db_fl.lib (target)
frame_npc_db_ps.lib (PC simulation)

## Slide 52: Frame Body Concept – System Setup
Required Resources
Library RAM [kB] ROM[kB]
frame_na7_db_fl.lib 1.3 15.7
frame_na7_db_ir.lib 0.0 7.8
misc_na7_db_fl.lib 0.1 1.0
misc_na7_db_ir.lib 0.0 0.2
tif_na7_db_fl.lib 0.6 7.0
tif_na7_db_ir.lib 0.0 0.8
osx_na7_db.lib 0.1 0.9

## Slide 53: Frame Body Concept
Overview
Frame Functionality & Interfaces
Test Interface
System Setup
Layer 1 Interface

## Slide 54: Frame Body Concept - Layer 1 Interface
CONDAT
Layer 2/3 Entities
pei_
Frame vsi_
Virtual OS
OS Extensions:
Passive Model
Routing
Trace
Memory Supervision
Timer Configuration
Startup
TI
Layer 1 asynchronous
pei_
OSX
vsi_
TI
Layer 1
synchronous

## Slide 55: Frame Body Concept - Layer 1 Interface
MM
L1A
L1S
PPC/ALR
RR
DL
Condat Layer 2/3
TI Adaptation
TI Layer 1
IRQ
Func()
Func()

## Slide 56: Frame Body Concept - Layer 1 Interface
INT_Initialize()
INC_Initialize()
App_Initialize()
TaskEntry()
L1A_task()
os_alloc_prim()
os_send_sig()
vsi_c_send()
vsi_c_new()
...
...
RESET
Startup and L1 Frame Access
....
L1S_HISR()
TI
OSX
CONDAT
NUCLEUS
RTOS

## Slide 57: Frame Body Concept - Documentation
Frame Users Guide 8434.100
VSI/PEI Interface Description 8415.033
OS Interface Description 8415.036

## Slide 58
END