## Slide 1: Generic Software Platform
Mathias Punger
January 19th, 2005

## Slide 2: Agenda
Software Architecture
Components of the Generic Software Platform
Test Features of the Generic Software Platform
Current Status

## Slide 3: Embedded Systems Software Architecture
APP: Software running on device (protocol stack, multimedia, PIM)
DRV: High-level application drivers (use RTOS services)
RTOS: Abstracts from HW and manages resource sharing
BSP: Basic HW support to boot system, low-level drivers
HW: Mobile phone chipset including MCU, DSP and Peripherals
Hardware (HW)
Board Support Package (BSP)
3rd Party Operating System (RTOS)
App Drivers (DRV)
Application Software (APP)

## Slide 4: Hardware Example
Digital Baseband Chip for GSM/GPRS/UMTS
The software in a mobile phone is executed on the MCU and DSP of the Digital Baseband chip.
MCU ARM9
DSP 320C55x
RAM
ROM
RAM
FLASH
UART
USB
MEMORY CTRL
AUDIO
GSM GPRS
UMTS
TBB4105
ABB
RF

## Slide 5: Application Software Example
Software Entities running in different RTOS threads implement the GSM protocols
Message based Communication between software entities
Nearly all software entities use RTOS services like timers, memory,...
Extensive tests of software entities mandatory
L1
RR
MM
CC
SS
SMS
ACI
MMI
SIM
DL
GSM Protocol Stack for Mobile Phones

## Slide 6: Embedded Systems Software Architecture
Challenge: Different operating systems need to be supported (Nucleus, Linux, Symbian, ...)
Drawback: The application software is dependent on the RTOS.
Objective: Keep application software operating system independent.
Conclusion: Introduction of the Generic Software Platform (GSP)
Hardware (HW)
Board Support Package (BSP)
3rd Party Operating System (RTOS)
App Drivers (DRV)
Application Software (APP)

## Slide 7: Embedded Software Architecture with GSP
Application Software accesses the Operating system through the Generic Software Platform (GSP) and remains OS independent.
HW
BSP
3rd Party RTOS
Application Software
App Drivers
Generic Software Platform (GSP)

## Slide 8: Software Architecture with GSP
HW
BSP
3rd Party RTOS
OS Abstraction Layer
Support Drivers
Common Services
Entity Environment
Common Entities
Application Entities
App Drivers
In addition to the RTOS abstraction GSP provides several services needed to run and test the application entities.

## Slide 9: GSP Components
Abstraction of Operating System API
OS dependent diagnose
OS dependent start-up
OS Abstraction Layer

## Slide 10: GSP Components
OS Services
  Threads
  Memory
  Messaging
  Timers
  Semaphores
Proprietary Services
  Trace (printf)
  Message routing
Supervision
  Memory
  Stack
Common Services

## Slide 11: GSP Components
High level startup
  Initialization
  Creation/Start of threads
Programming environment
  Main loop of threads
  Message dispatcher
Entity Environment

## Slide 12: GSP Components
Test interface
  Send messages to tools
  Receive messages from tools
Diagnose and crash handling
  Handle CPU exceptions
  Store CPU state at crash time
  API to handle errors/warnings
Common Entities

## Slide 13: GSP Components
Test tool connectivity
  Message protocol
  Access to UART, USB, Ethernet
Support Drivers

## Slide 14
OS Interface
provides interface to RTOS services
  Threads
  Low-level memory management
  Queues
  Timers
  Semaphores
  Interrupts
  Diagnosis
OS Abstraction Layer
Common Services
OS
Generic Software Platform - Interfaces

## Slide 15
GSP Interface
Entity/thread services
High-level memory management
Messaging (send, receive)
Timer services (single shot, periodic)
Semaphore/mutex
Trace services
Common Services
Common Entities
Application Entities
GSP
Generic Software Platform - Interfaces

## Slide 16: Generic Software Platform - Interfaces
Software Entity Interface (SEI)
Provides interface of a software entity
  creation
  initialization
  message passing
  timeouts
The SEI needs to be implemented in each GSP based software entity
Interface functions are exported by the software entity (not statically linked)
Entity Environment
SEI
SEI
Common Entities
Application Entities
I
I

## Slide 17: Exchange of Operating System
HW
Nucleus BSP
Nucleus RTOS
OS Layer Nucleus
Support Drivers
Common Services
Entity Environment
Common Entities
Application Entities
App Drivers
Linux BSP
Linux OS
OS Layer Linux
Changing from Nucleus to Linux
Exchange OS Layer, RTOS and BSP
Application software and major parts of GSP remain unchanged

## Slide 18: GSP Test and Debug Functionality
Message Duplication, monitor communication in PCO
Message Redirection, run test scripts with TAP
Tracing, view debug information in printf() format in PCO
all filters are set dynamically (not at compile time)
TAP
SWE C
SWE A
SWE B
SWE A
SWE B
PCO
SWE A
SWE B
PCO

## Slide 19: GSP Tools for Testing
Trace Viewer (PCO)
display traces
decode routed messages
set dynamic configuration
Test Application (TAP)
run test scripts

## Slide 20: GSP in Target and Tools
Application Entities
PC
Windows
TAP
PCO
Target System
PC
Serial, USB, Ethernet
Link target system to PC via test interface and connect TAP and/or PCO
Log message exchange between the software entities in target system
Log traces and routed messages sent by the software entities in target system
Run testcases (send a messages into the target and check the response)
Additional GSP based tools can be designed to run on PC
GSP
GSP

## Slide 21: GSP on MCU and DSP
GSP running on MCU(ARMx) and DSP(TMS320C5x)
GSP-‘light‘ on DSP due to memory constraints
Identical GSP API on MCU and DSP for services existing on both
Transparent location (no need to know own location for most services)
Transparent communication (no need to know location of partner)
MCU
DSP
Application Entities
GSP
GSP
Application Entities
GSP

## Slide 22: State of Generic Software Platform
Operating Systems:
Nucleus (ARM, MNT)
Linux (kernel space, user space, RT Linux)
Symbian (feasibility study done)
WinCE (feasibility study planned)
Win32 for test tools
pSOS, Vxworks (currently no support)
DSP/BIOS (planned to run on DSP)
Test interface drivers supported:
UART
Simulated UART (Shared memory)
Socket
USB

## Slide 23: Conclusion
GSP supports you in
designing operating system independent software
reducing time to market by reuse of existing software
increasing software quality by using built-in test functionality