## Slide 1
PCO for LTS
filtering
(ID: 6519.022.01.001)

## Slide 2: PCO for LTS … overview
Basics
Filters on board
Soft filters

## Slide 3: PCO for LTS … Basics
For communication with the outer world a dedicated entity is used: Testinterface (TST)
  serial port configuration:
    default baudrate: 38400
    default flow control: none
    default data bits: 8
    default stop bits: 1
    default parity: none
  data is send in blocks enclosured by
    StartOfText-Byte (STX): 0x02 … send before any byte-block
    LineFeed-Byte (LF): 0x0a … send after any byte-block
Mobile
TST
Gateway
STX|data-block|LF

## Slide 4: PCO for LTS … Basics
At Condat we use the following block types:
  Trace … a text string send by an entity to an outside test system
  Primitive … a structure send from one entity to another
  Air message … an encoded structure send within a primitive
Concerning PCO we distinguish between:
  PCO message … a message send between PCO components (server, viewer, controller)
  PCO primitive … a data block coming from mobile -> has to be interpreted by PCO components

## Slide 5: PCO for LTS … Basics
Mobile
Traces:
  time and size are represented by character numbers (e.g. “1223”) !
Frame
TST
MM
RR
Gateway
Testsystem
PCO

## Slide 6: PCO for LTS … Basics
Mobile
Primitives:
  time, size and opc are represented by character numbers (e.g. “1223”) !
Frame
TST
MM
RR
Gateway
Testsystem
PCO

## Slide 7: PCO for LTS … Basics
Mobile
Air-messages:
  time, size and opc are represented by character numbers (e.g. “1223”) !
Frame
TST
MM
RR
Gateway
Testsystem
PCO

## Slide 8: PCO for LTS … Basics
PCO messages:
  currently implemented by Syst_prim using T_SYST_PRIM-struct from FRAME/TST
  time and size are represented binary
PCO primitives:
  currently same structure as PCO messages
    for direct Testing with xPanel or TAP ok, since the testinterface reformats the incoming binary-blocks into a T_SYST_PRIM-structure
    for LTS this could be done by PCO-server but maybe with new structure (e.g. because of time stamp issues)
    … or the viewer would have to interpret PCO-primitives as binary-blocks itself

## Slide 9: PCO for LTS … Filter on board
Advantages of filtering on mobile already:
  traffic reduction
  necessary to receive primitives/air-messages
Usage:
  several CONFIG-primitives (‘S’ as first header byte) are send to the mobile

## Slide 10: PCO for LTS … Filter on board
Mobile
Trace filters:
  config string of form “TRACECLASS <ClassMask>” sent to an entity
  example: “TRACECLASS FF” --> MM “TRACECLASS 00” --> RR
Frame
TST
MM
RR
Gateway
Testsystem
PCO
#define TC_FUNC 0x01
#define TC_EVENT 0x02
#define TC_PRIM 0x04
#define TC_STATE 0x08
#define TC_SYSTEM 0x10
#define TC_ISIG 0x20
#define TC_ERROR 0x40

## Slide 11: PCO for LTS … Filter on board
Mobile
Primitive filters:
  config string of form “{<OrgDestination>|ALL}[<opc mask>] <AddDestination>” sent to an entity
  example: “DUPLICATE MM PCO” --> RR
Frame
TST
MM
RR
Gateway
Testsystem
PCO

## Slide 12: PCO for LTS … Soft filters
Advantages of filtering on test system side:
  filter on primitive structure level
  filter on air-message level
Usage:
  implementation on PCO-server or PCO-viewer
    on primitive level (sender, receiver, OPC)
    on primitive structure level -> CCDEdit needed
    on air message level -> CCDEdit and CCD needed
Mobile
Gateway
Testsystem
PCO server
PCO viewer
screen