## Slide 1
PCO
Features Overview
General Overview
Filtered Tracing
Structure Interpretation
Logging, Replay and Testcase Generation
Integration with other Tools
Scripting

## Slide 2: PCO … features overview
General Overview
PCO – Point of Control and Observation
  control of the PS behaviour and produced traces via system commands
  observation of all kinds of states and the data flow inside the PS
Online and offline mode available
Freely combinable set of GUI applications and scriptable command line tools
Open interface to derive customized viewers
  e.g., a dedicated Engineering Mode Window is under development
Protocol stack
(real target or PC simulation)
PCO
(combined with other test tools)
Test interface (UART, Socket, SHM,…)
Traces, duplicated primitives and air messages
System commands, keystrokes
Log files
Record
Replay
Online
Offline

## Slide 3: PCO … features overview
Filtered Tracing
Traces, primitives and air messages can be watched ...
  in one or more customized windows
  synchronized among all layers (L1 and L2/3)
  distinguishable by colors
Compression of traces at the test interface
Observation of dedicated parameters
  e.g., neighbor cell count
Various kinds of filters may be applied
  per SAP
  per entity
  per primitive/air message

## Slide 4: PCO … features overview
Structure Interpretation
Hexdumps of duplicated primitives are interpreted
  the individual values of elements are shown
  ... together with cleartext explanations
Air messages are decoded
  and interpreted as well

## Slide 5: PCO … features overview
Logging, Replay and Testcase Generation
All data received via the test interface can be
  recorded into logfiles
  replayed, e.g., with different filter settings
  used to automatically generate new (regression) test cases
Lab-Test
Test-Case Generator
Logfile
100010010100 011001110110
Field-Test
Development & Bug-Fixing
PCO
Replay

## Slide 6: PCO … features overview
Integration with other Tools (1)
Export functions for various file formats (e.g., ASCII) exist
Already a lot of tools can be directly used on the current viewer entries ..
  for example MSCView to watch the corresponding message flow

## Slide 7: PCO … features overview
Integration with other Tools (2)
Many tools exist which use the same framework as PCO
  ... and can, therefore, run in parallel as needed
Some of them are usually started automatically by PCO
  ... for example the virtual mobile „xPanel“
In further cases parts of PCO are started by other applications
  ... like the Test Application Process:

## Slide 8: PCO … features overview
Scripting
PCO also comes with various command line tools ...
  to control the logging/replay process
  to do converting
  to send system commands to the protocol stack
  ...
The PCO Reaction Viewer component ...
  monitors incoming traces
  ... and starts actions triggered by rules defined in a deticated XML file, e.g.:
    sending of system commands
    starting of applications

## Slide 9: PCO … features overview
Live Demonstration

## Slide 10
Thanx for your patience 