## Slide 1
Testing with
xPanel & PCO2
(an introduction)

## Slide 2: xPanel & PCO2 … outline
General Concept
Usage of the Tools
Overview
Logging and Replay
Filter Setup
Communication Setup
Parameter Observation
Important Files
Background
Dataflow
Interpreting/Decoding
Software Layers
Configuration Files

## Slide 3: xPanel & PCO2 … general concept
Test interface approach:
  data interface between G23 protocol stack and a PC test system
  usually a standard serial cable, COM-ports on both ends
Protocol stack
PC test system
Test interface
Traces, duplicated primitives
System primitives, keystrokes

## Slide 4: xPanel & PCO2 … general concept
On PC test system side:
  test interface executable using the GPF-FRAME
    connects via standard OS drivers
  used by tools like the former PANEL
  .. and of course by xPanel & PCO
  these tools finally provide GUI-stack-access for testers
On stack side:
  test interface entity included in the GPF-FRAME
  uses corresponding hardware driver for communication

## Slide 5: xPanel & PCO2 … general concept
xPanel - eXtended Panel:
  capable to display text & graphics output of mobile MMI
  mutable layout, easy to change
PCO2 - Point of Control and Observation:
  filtered watching of traces and duplicated primitives
  intuitive configuration (traceclasses, routing) of protocol stack
  server, controller, extensible set of viewers

## Slide 6: xPanel & PCO2 … outline
General Concept
Usage of the Tools
Overview
Logging and Replay
Filter Setup
Communication Setup
Parameter Observation
Important Files
Background
Dataflow
Interpreting/Decoding
Software Layers
Configuration Files

## Slide 7: xPanel & PCO2 … usage overview
“Take off”:
  starting of pco2.bat in the bin-directory (ClearCase: \gpf\BIN) …
  will per default result in such a scenario:
PCO-Controller
PCO-Server
xPanel
PCO-Viewers

## Slide 8: xPanel & PCO2 … usage overview
The xPanel:
  can be used like a real mobile
    to press keys (e.g. for switching on)
    to see display output
  provides interface to send FRAME system primitives and AT-commands
  provides GUI to select communication type
  is easily adaptable to your layout

## Slide 9: xPanel & PCO2 … usage overview
The PCO-Viewer(s):
  configuration can be stored as a “.svc”-file
  watch traces of selected entities
    ordered by time
    distinguished by colors
  watch redirected primitives/messages
    as hexdump
    as structure
  filter by sender or OPC

## Slide 10: xPanel & PCO2 … usage overview
Compressed Tracing with Str2Ind-Tables:
  after loading of the table all traces will be shown as expected
  initially no table for interpretation of Trace-IDs is loaded
  after reset or by explicit request
    PS sends a version number
    Viewer searches for matching .tab-file in specified directory structure
  for performance and memory reasons traces are compressed at compile time
  each PS build creates a str2ind-table containing [ID]->[Trace string] combinations

## Slide 11: xPanel & PCO2 … usage overview
  Function traces …
Types of traces shown by PCO-Viewer:
  Event traces …
  Primitive traces …
  State traces …

## Slide 12: xPanel & PCO2 … usage overview
  receives all traces and redirected primitives from the target
    forwards them to viewers
    may store them into logfiles
The PCO-Server:
  for replay it can forward logged data to viewers, too
  may insert extra timestamp traces
  is controlled by the PCO-Controller

## Slide 13: xPanel & PCO2 … usage overview
The PCO-Controller:
  is actually executed by pco2.bat and starts a configurable set of other applications, like xPanel
  provides access to PCO-Server
    to start logging of data
    to replay logged data
  allows sending of FRAME system primitives to the protocol stack (via PCO-Server)
    from direct user input
    out of a pool of predefined system primitives loaded from a dedicated file (usually View.txt)
    by selections in a matrix (stored per default in pco_stack.xml) which may be ex-/imported
  enables setup of the communication drivers to be used
  on exit: shuts down all initially started applications
    called the “test environment”

## Slide 14: xPanel & PCO2 … logging and replay
Logging / Recording:
  specify name of test session
  start logging process
  now every trace/primitive received via the test interface will be logged
    Independent of any filter setting in a PCO-Viewer
  PCO-Server appears green
  after pressing the “STOP” button …
    a <session name>.pco file can be found in the current session dir of PCO-Server
    a copy of (selected parts of) the logged session can be stored somewhere else (and, e.g., be sent to developers)
  PCO-Server appears red again

## Slide 15: xPanel & PCO2 … logging and replay
Replay:
  select test session name
  or drag/drop .pco-file to PCO-Controller
  press the „PLAY“ button
  PCO-Server appears yellow
  now logged traces/primitives will be replayed in connected PCO-Viewers
    depending on the individual filter settings
  pausing and repositioning are possible

## Slide 16: xPanel & PCO2 … filter setup
Trace/primitive filtering is done in two stages:
Logfile
  Protocol
  Stack
  PCO-Controller
  Matrix
  “Hard”-Filter
  “Soft”-Filter
  PCO-Viewer
  Filter
  PCO-Viewers

## Slide 17: xPanel & PCO2 … communication setup
PCO-Controller:
Protocol stack
TST (Testinterface)
Serial cable
Multiplexer
Network
Shared memory
  configuration of test interface
  evtl. start of extra tools
  selection of mode
  secification of individual parameters

## Slide 18: xPanel & PCO2 … communication setup
  for convenience several default configurations exist
  it has to be ensured that a matching ccddata-DLL is selected
    either a DLL which has been delivered together with the PS-image
    or a prebuild DLL from ...\ccddata\ (e.g. ccddata_G23M_333_S64.dll for older B-Sample-Releases)
PCO-Viewer:

## Slide 19: xPanel & PCO2 … communication setup
  choose COM port
Communication via TraceMultiplexer:
  if using the TraceMultiplexer for the first time it has to be configured:
  the green tray symbol signals a successful connection
  select baudrate of 115200
  disable flow control

## Slide 20: xPanel & PCO2 … parameter observation
Parameter observation is a special feature of PCO-Viewer ...
  allowing to filter specific strings out of traces
  ... and displaying them in an extra sub-window
First you have to …
  find out how traces containing the wanted parameter look like
  … or request specific traces from the developer
Afterwards you must …
  translate an example trace into a mask
  … where the actual parameter values are exchanged by a placeholder starting and ending with ‘%’-characters, for example: “--- IN:%Last primitive%-”
This mask can now be added to the list …
  by opening the options dialog, e.g., via the menu entry “view/options…”
  ... and together with more settings, like the entity

## Slide 21: xPanel & PCO2 … parameter observation
Attention! The sender entities of the expected traces containing parameters have to be in the watch list of the PCO-Viewer filter!
Now the latest parameter values ...
  can be watched in the special sub-window
  ... together with their historical values depending on the setting in the options dialog
Values in this grid ...
  can be copied to clipboard
  ... and sorted
A click on a value ...
  moves the main entry list to the corresponding trace

## Slide 22: xPanel & PCO2 … important files
Volatile files:
  have to be build together with the used protocol stack
    ccddata_dll.dll (database with primitive symbols)
    str2ind.tab (table with “ID <-> trace text” associations)
Detailed documentation:
  pco_userguide.doc (ClearCase: \gpf\DOC\pco\pco_userguide.doc)
  xpan_userguide.doc (ClearCase: \gpf\DOC\xpanel\xpan_userguide.doc)
  xPanel_plus_design_spec.doc (ClearCase: \gpf\DOC\xpanel\xPanel_plus_design_spec.doc)
    contains requirements for a graphical display-driver
  frame_users_guide.doc (ClearCase: \gpf\DOC\frame_users_guide.doc)
    contains description of FRAME system primitives
  pco_intro.pps (this document) (ClearCase: \gpf\DOC\pco\pco_intro.pps)

## Slide 23: xPanel & PCO2 … outline
General Concept
Usage of the Tools
Overview
Logging and Replay
Filter Setup
Communication Setup
Parameter Observation
Important Files
Background
Dataflow
Interpreting/Decoding
Software Layers
Configuration Files

## Slide 24: xPanel & PCO2 … data flow
TST
Protocol
Stack
TST
Target
Test system
primitives
traces
PCO logfile
duplicated primitives,
traces
PCO
view
PCO
viewers
CCD-data
decode interprete
X
Panel
primitives (display, keyboard)
PCO
server
traces
duplicated primitives
control
PCO
controller
system primitives

## Slide 25: xPanel & PCO2 … interpreting/decoding
What for do I need a ccddata-DLL (e.g. ccddata_dll.dll) ?
  contains information about all primitive and air message structures used in the corresponding protocol stack
Without:
With a matching DLL:

## Slide 26: xPanel & PCO2 … software layers
FRAME
FRAME
Div.
Entities
(PS)
TST
TST
Windows, Linux, ...
Nucleus, PSOS, ...
VCMS
Target
Test system

## Slide 27: xPanel & PCO2 … software layers
PCO
view
VCMS
Windows, Linux, ...
Nucleus, PSOS, ...
FRAME
FRAME
Div.
Entities
(PS)
TST
TST
Target
Test system
PCO
view
PCO
view
CCD-data
X
Panel
PCO
server
PCO
control

## Slide 28: xPanel & PCO2 … software layers
PCO
view
Windows, Linux, ...
Nucleus, PSOS, ...
VCMS
FRAME
FRAME
Div.
Entities
(PS)
TST
TST
Target
Test system
X
Panel
PCO
server
PCO
control
PCO
view
TAP
PCO
view
CCD-data

## Slide 29: xPanel & PCO2 … software layers
Windows, Linux, ...
VCMS - cms.dll
FRAME
frame.dll tif.dll misc.dll
TST tst.exe
xPanel xpanel.exe,
xpanel.tcl
PCOserver
pco_srv.exe
PCOcontroller pco_ctrl.exe
PCO
view
PCO
view
PCOview pco_view .exe
CCD-database ccddata_*.dll
Mapping to executables and DLLs:

## Slide 30: xPanel & PCO2 … configuration files
  xpan.ini (ClearCase: \gpf\cfg\xpan.ini)
    contains all settings for xPanel
    like communication port and baudrate (if xpanel is used alone)
xPanel configuration files:
  TARGET_lo.tcl (ClearCase: \gpf\cfg\TARGET_lo.tcl)
    default layout for xPanel
    here e.g. new keys may be added

## Slide 31: xPanel & PCO2 … configuration files
  pco.ini (ClearCase: \gpf\cfg\pco.ini)
    contains all settings for the PCO components
PCO configuration files (1):
  pco_start.lst (ClearCase \gpf\cfg\pco_start.lst)
    list with applications to be started
    like xPanel, PCO-viewers
    editable by GUI (PCO-Controller)

## Slide 32: xPanel & PCO2 … configuration files
PCO configuration files (2):
  View.txt (ClearCase: \gpf\cfg\View.txt)
    contains predefined FRAME system primitives e.g. “DUPLICATE MM PCO” -> RR “CONFIG AT+CFUN=1” -> MMI (to send At-Commands)
    these may be selected and sent using the PCO-Controller

## Slide 33: xPanel & PCO2 … configuration files
PCO configuration files (3):
  pco_stack.xml (ClearCase: \gpf\cfg\pco_stack.xml)
    contains all “Matrix”-entries of the PCO-Controller
    may be edited to e.g. change the entry-order

## Slide 34
Thanx for your patience !

## Slide 35: xPanel & PCO2 … TI internal issues
Maintenance and versions:
  xPanel and PCO are maintained by the GPF-team
  delivery is usually done inside the gpf_x.csi file included in the ConfigSpec of each developer
  local setup-packages can be obtained at \\dbgs2\deveng\cc\gpf\projects\pco\delivery\index.html
Build of ccddata_dll.dll:
  automatically done while running makcdg-script
  default output dir: \gpf\BIN
Build of str2ind.tab:
  automatically done during protocol stack build
  default output dir: \g23m\__out__\...\trace\...
Complaining:
  can be done directly by using the “moan”-button in the system tray
  see \gpf\DOC\moanbtn\mbtn_userguide.doc