## Slide 1
Running Test Cases with
TAPCaller
(an introduction)

## Slide 2: TAPCaller … overview
General concept
Preparations
Usage with old TAP
Usage with TAP2 and PCO2
Important files

## Slide 3: TAPCaller … general concept
test interface approach:
  data interface between G23 protocol stack and a PC test system
  for running test cases: usually shared memory on one PC
TAPCaller,
TAP2,
xPanel,
PCO2,
...
Test interface
System primitives
RR
PC test system
Protocol stack
Traces
Protocol primitives
duplicated primitives
redirected primitives
MM

## Slide 4: TAPCaller … general concept
On PC test system side:
  test interface executable using the FRAME
    connects using standard OS drivers
  used by tools like xPanel
  .. and of course by TAP2 & PCO2
On stack side:
  test interface entity included in FRAME
  uses corresponding hardware driver for communication

## Slide 5: TAPCaller … general concept
PCO (Point of Control and Observation):
  tools cabable to stimulate the protocol stack and display traces and duplicated primitives
  used here for logging and replaying test sessions
TAP (Test Application Process):
  program which executes test cases by sending, receiving and comparing primitives to/from the protocol stack
TAPCaller:
  GUI-tool for easy handling TAP and PCO

## Slide 6: TAPCaller … general concept
FRAME
FRAME
Div.
Entities
(PS)
TST
TST
Windows, Linux, ...
Nucwin, Nucleus, …
VCMS
Protocol stack
Test system
The software layers:

## Slide 7: TAPCaller … general concept
Windows, Linux, ...
Nucwin, Nucleus, …
VCMS
FRAME
FRAME
Div.
Entities
(PS)
TST
TST
Protocol stack
Test system
PCO
view
PCO
view
The software layers:
PCO
view
CCDedit
TAP2
PCO
server
TAP
Caller

## Slide 8: TAPCaller … preparations
Build of necessary executables:
  before testing some executables have to be (re)build after each run of makcdg:
    the protocol stack – in any case ;-)
    tap2_{gprs|gsm}.exe (ClearCase: \gpf\BIN\tap2_xxx.exe)
      old TAP for usage without PCO2
      call gnumake in \gpf\TAP
    ccddata_dll.dll (ClearCase: \gpf\BIN\ccddata_dll.dll)
      used by new TAP2 (tap2.exe) and PCO2
      automatically build by makcdg-script

## Slide 9: TAPCaller … preparations
Optional modification of test cases:
  To receive not only traces but also duplicated primitives while testing ...
  …
  COMMAND (“L2R REDIRECT MMI TAP”)
  | | |
  COMMAND (“TAP REDIRECT TAP L2R”)
  …
  ... extra system primitives have to be inserted into the test document (e.g. l2r_steps.cpp)
  …
  COMMAND (”L2R DUPLICATE MMI PCO”)
  COMMAND (“L2R REDIRECT MMI TAP”)
  | | |
  COMMAND (“TAP DUPLICATE TAP PCO”)
  COMMAND (“TAP REDIRECT TAP L2R”)
  …

## Slide 10: TAPCaller … preparations
Build of test cases:
  Generators
    doc2txt
    xgen
    ccdgen
  Compilers
    msdev / cl
    (mktc)
SAP
Document
GRR.DOC
TDC
Testcases
GRR.dsp
Compilers
Linker
Testcase DLL
“makcdg tdclib”
Primitive / Message Constants and Structs
p_grr_val.h
  For more informations see:
    protocol_stack_testing.ppt
    8415_028.doc (ClearCase: \GPF\DOC\8415_028.doc)

## Slide 11: TAPCaller … preparations
Selection of test cases:
  Start tapcaller.bat (ClearCase: \gpf\BIN\tapcaller.bat)
  enable testcases from DLL(s)
  choose directory

## Slide 12: TAPCaller … preparations
Protocol stack (PS) selection:
  Start a protocol stack by your own, e.g. inside VisualStudio ...
  ... or specify an executable ...
  ... and enable automatic start of PS (before each test case execution)

## Slide 13: TAPCaller … usage with old TAP
Protocol
Stack
TST
Protocol stack
Test system
Data flow:
TAP
Caller
TAP2
TST
Start Stop
.dbg
files
RR
MM
Trace
windows
primitives
traces
Testcase DLL

## Slide 14: TAPCaller … usage with old TAP
Test system
Snapshot:
primitives
traces
Start Stop
TAP2
tap2_gprs.exe
Protocol stack

## Slide 15: TAPCaller … usage with old TAP
Configuration:
  select TAP executable which has to be rebuild after each makcdg call ...
  ... and choose „old TAP“-mode
  evtl. modify communication type, if testing with a real target

## Slide 16: TAPCaller … usage with TAP2 & PCO2
Protocol
Stack
TST
TST
Test system
PCO
server
Data flow:
TAP
Caller
TAP2
start stop
.dbg
files
PCO logfile
control
Protocol stack
PCO
view
PCO
viewers
duplicated primitives,
traces
primitives
primitives
traces
Testcase DLL
traces
duplicated primitives
CCDedit
decode interprete

## Slide 17: TAPCaller … usage with TAP2 & PCO2
Snapshot:
  testcase running
PCO-Server
primitives
traces
TAP2
tap2.exe
TST
tst.exe
Test system
start stop
control
PCO-Viewer
traces, duplicated primitives
Protocol stack

## Slide 18: TAPCaller … usage with TAP2 & PCO2
Snapshot:
  testcase replay
PCO-Server
Test system
control
PCO-Viewers
traces, duplicated primitives

## Slide 19: TAPCaller … usage with TAP2 & PCO2
Configuration (1):
  select path to tap2.exe ...
  ... and deselect „old TAP“-mode
  evtl. modify communication type, if testing with a real target

## Slide 20: TAPCaller … usage with TAP2 & PCO2
Configuration (2):
  enable logging with PCO ...
  ... and choose path to PCO executables (should be the same as for tap2.exe)
  evtl. select a viewer configuration, with which a PCO-Viewer should be started while running testcases

## Slide 21: TAPCaller … important files
Executables and DLLs:
Windows, Linux, ...
VCMS - cms.dll
FRAME
frame_wn.dll tif_wn.dll misc_wn.dll
TST tst.exe
TAP2 tap2.exe
(tap2_gprs.exe)
PCOserver
pco_srv.exe
PCO
view
PCO
view
PCOview pco_view .exe
CCDedit ccddata_dll.dll, ccddata_load.dll
TAP
Caller tapcaller.exe

## Slide 22: TAPCaller … important files
  pco.ini (ClearCase: \gpf\BIN\pco.ini)
    contains all settings for the PCO components
  *.svc-files
    Standard-Viewer-Configuration files
    tap.svc.default -> default viewer config, will be copied to tap.svc by tapcaller.bat
PCO configuration files:
TAPCaller configuration files:
  *.tcc-files
    TAP-Caller-Configuration files

## Slide 23: TAPCaller … important files
Volatile files:
  have to be build together with the used protocol stack
    ccddata_dll.dll (table with primitive symbols)
    str2ind.tab (table with trace texts - introduced with GPRS_1.3.2)
Detailed documentations:
  tapcaller_userguide.doc (ClearCase: \gpf\DOC\tapcaller\tapcaller_userguide.doc)
  pco_userguide.doc (ClearCase: \gpf\DOC\pco\pco_userguide.doc)
  frame_users_guide.doc (ClearCase: \gpf\DOC\frame_users_guide.doc)
  testplatform_userguide.doc (ClearCase: \gpf\DOC\testplatform_usersguide.doc)
  tapcaller_intro.ppt (this document) (ClearCase: \gpf\DOC\tapcaller\tapcaller_intro.ppt)

## Slide 24: TAPCaller … TI internal issues
Maintenance and versions:
  TAPCaller, TAP and PCO are maintained by the GPF-team
  delivery is usually done inside the gpf.csi file included in the ConfigSpec of each developer
  the very newest version can be obtained by including gpf_testtools.csi right after “mkbranch xxx” (at least before gpf.csi) in the ConfigSpec
Complaining:
  can be done directly by using the “moan”-button in the system tray
  see \gpf\DOC\moanbtn\mbtn_userguide.doc